## Slide 1: Cisco STA1520 Tuning Adapter
Dan Hisaw, Engineer.Customer Support

## Slide 2: Dan Hisaw
ENGINEER.CUSTOMER SUPPORT

## Slide 3: Course Objectives
  Understand the purpose of the Cisco STA1520 Tuning Adapter.
  Understand the interface between the Tuning Adapter and the UDCP (typically a TiVo).
  Understand the Tuning Adapter diagnostic screens.

## Slide 4: Course Flow
A
M
P
M
Day 1 | Day 2 | Day 3 | Day 4 | Day 5
Course Introduction Designed as a “Lunch and Learn” | N/A | N/A | N/A | N/A
Lunch |  |  |  | 
State the objectives and go through a short presentation. | N/A | N/A | N/A | N/A

## Slide 5: STA1520 Tuning Adapter
STA1520 Tuning Adapter looks like an RNG-100 NGP STB but has very significant modifications to the case, board, and NGP software.
The TA does NOT have audio/video capabilities.
There is NO communication between the Tuning Adapter and the TiVo over the RF connection.
All communication between the Tuning Adapter and the TiVo goes over the USB cable (resolve_tuning_req, resolve_tuning_rsp, channel_table_req, channel_table_rsp, channel_table_update, etc ).
Single LED on front panel.
Blinking patterns for the LED documented in Cisco document “Staging the Tuning Adapter” (P/N 4025012 / EDCS-976128).

## Slide 6: Tuning Adaper and UDCP (TiVo) Connections

## Slide 7: Tuning Adapter Acronyms
TA – Tuning Adapter.
TR – Tuning Resolver (original name for Tuning Adapter).
UDCP – Unidirectional Digital Cable Product (CableLabs-speak for a TiVo).
TiVo – Not an acryonym, but the most commonly-known UDCP.
USB – Universal Serial Bus. A USB 2.0 cable connects the Tuning Adapter and the TiVo to allow “Resolve Tuning Messages” and other messages defined in the CableLabs Tuning Resolver Interface Specification (OC-SP-TRIF-I03-090206) to be sent between the Tuning Adapter and the TiVo.

## Slide 8: Tuning Adapter, TA (formerly Tuning Resolver, TR)
The CableLabs spec is called the Tuning Resolver Interface Specification. (Links to Interim Specifications I03 and I04 appear below):
http://cablelabs.com/specifications/OC-SP-TRIF-I03-090206.pdf
http://www.cablelabs.com/specifications/OC-SP-TRIF-I04-110204.pdf

## Slide 9: Tuning Adapter Functional Diagram
Source: http://cablelabs.com/specifications/OC-SP-TRIF-I03-090206.pdf
TiVo
Tuning Adapter (SDV Client)

## Slide 10: Tuning Adapter Overview
Concept Definition:
  TA is an external MSO-provided adaptor that enables a UDCP (Unidirectional Cable Product) to access all linear channels (switched or broadcast)
Key Product Features / Functions:
    DSG Modem & Client Controller
    Legacy OOB RDC/FDC
    CPU & memory
    SDV application
With Cable Card
Tuning Adapter has embedded security
Cable Card goes in the TiVo
Slide: Cisco Engineering (author unknown)

## Slide 11
Tuning Adapter in a Cisco System (SARA Environment)
In a SARA Environment, TAs receive SDV information -- including the channel map -- in the same manner that STBs do.
TR Config File support has never been implemented on the SARA App Server
Despite the fact that the UDCP (TiVo) has a Cable Card in it, with a TA connected, the UDCP gets its channel map from the TA.
TiVo
Slide: Cisco Engineering (author unknown)

## Slide 12
Tuning Adapter in a Cisco System (Non-SARA Environment)
In a Non-SARA Environment, TAs receive SDV information -- including the channel map -- via the Channel Definition File as described in a Cisco provided document: “Tuning Resolver Configuration File Format Specification”
TR Config File support has been implemented on the TWC Mystro Application Server (MAS)
Despite the fact that the UDCP (TiVo) has a Cable Card in it, with a TA connected, the UDCP gets its channel map from the TA.
TiVo
Slide: Cisco Engineering (author unknown)

## Slide 13: Tuning Adapter Config File (Replaces SAM for non-SARA Sites)
May be referred to on as the “TA Config File” or the “TR Config File
TA diag screens: It is referred to as the “TA Config File” on the diag page titled “Tuning Resolver.” (Nice consistency!)
The TR Config file can contain the Mini Carousel Scan List frequencies and modulation format.
BFS path name (URL)
  bfs:///msoconfig/sdv/<hub ID>/trconfig.tbl
BFS (Absolute Path on DNCS): We have seen these 2 at TWC MDN/ODN sites:
  /dvs/dvsFiles/BFS/DNCS/msoconfig/sdv/<hub_ID>/trconfig.tbl
  /export/home/dncs/mystro/bfs/msoconfig/sdv/<hub_ID>/trconfig.tbl
The generation of the TR Config File and its being published on BFS is the responsibility of 3rd parties like ATG (published from MAS Server).
There is a Cisco maketrconfig tool, but it is only meant for lab use. We cannot use this tool to generate TR Config Files for sites because this tool is not a scalable solution for managing site channel maps.
According to David Lutz (lutzd) in Development, there is no tool to parse the TR Config File. (This tool, if it existed, would do the opposite of what maketrconfig does.)

## Slide 14: Tuning Adapter – Packages and Security
The Cisco Tuning Adapter has embedded security. (The CableCARD goes in the TiVo)
The CableCARD goes in the TiVo (not the TA).
Only 2 packages go on the TA: The Brick package and the SDV package.)
All content packages (and the brick package) go on the CableCARD in the TiVo.

## Slide 15: The Cisco TA is a SARA Box (Needs SAM or a TR Config File)
The Cisco TA is a SARA box.
_SASD SAM Service stands for “Scientific-Atlanta Switched Digital”.
_SASD SAM Service is a SAM Service for both STBs and TAs for SDV Services.
_TASD SAM Service stands for “Tuning Adapter Switched Digital”.
_TASD is a SAM Service that can only be used by Tuning Adapters for SDV Services.
_TASD SAM Service allows BigBand sites to use BigBand’s load-on-boot SDV Client (BODClient.ptv) for set-tops and use _TASD for Tuning Adapters only. If you were to use _SASD, it would make it possible for SARA set-tops to become authorized for SDV (if the SDV package were put on the STB), and the embedded SDV Client in SARA would become active, resulting in 2 SDV Clients on the STB – the one embedded in SARA and BigBand’s load-on-boot app BODClient.ptv.
If both _SASD and _TASD are present in the SAM Table, _SASD takes precedence, so the TA will use _SASD and ignore _TASD according to David Lutz in Engineering (lutzd).
TR Config File replaces SAM for non-SARA sites. It is generated by a 3rd party like the MAS Server and published on BFS. The BFS path name (URL) is:
  bfs:///msoconfig/sdv/<hub ID>/trconfig.tbl

## Slide 16: Accessing the TA’s Diag Screens
The Cisco Tuning Adapter takes a signed image (.simg instead of .rom). Therefore, it is a Next Generation Platform box (NGP).
Before using cmd2000 on a Next Generation Platform box, you must use the sendPTEA.pl script to authorize the box for cmd2000 as shown below where “PTEA.msg” is the file containing the PassThru message to unlock cmd2000.
$ sendPTEA.pl PTEA.msg
Web diag pages. Open a Firefox on the DNCS and use URL http://<TA_ip_addr>:5030/0.html
http://10.1.0.238:5030/0.html (MAC 00:1C:EA:97:25:C4) is usually connected the one TiVo that Cisco IT has authorized to get through the corporate firewall to the TiVo Service. Currently, the TiVo connected to this TA MUST be connected to the yellow Ethernet jack in cube 5.1.241 in order to get through the firewall.

## Slide 17: TA Diag Page – Switched Digital Video
From Mini Carousel
1
3
4
5
6
7
2
Mini Carousel: CacheReady
A typical Charter site has SARA and BigBand SDV. These sites generally use a SARA Scan List to avoid the need for “dummy GQAMs”.

## Slide 18: TA Diag Page – SDV Mini Carousel
2

## Slide 19: TA Diag Page – SDV Session Info
“Ready”, not “Idle” or “Unavailable”

## Slide 20: TA Diag p. – Tuning Resolver (TR Config File)
TR Config File replaces SAM at non-SARA sites that don’t run saManager.

## Slide 21: TA Diag Page – UDCP (TiVo)
TiVo Connected to TA
TiVo Authorized

## Slide 22: Instructor Demonstration
Please watch as your Instructor demonstrates.

## Slide 23: Summary
  Remember that the “Tuning Adapter” spec from CableLabs still calls it a “Tuning Resolver”. Hence, the name “TR Config File” but sometimes people say “TA Config File”.
  The Cisco STA1520 is a SARA box running SARA code.
  Despite the fact that the STA1520 runs SARA code, in the absence of a SARA App Server, a TR Config File is generated by the 3rd-party App Server and these files are published on BFS.
  Generally there is 1 TR Config File per hub, resulting in 1 channel map per hub. However, you can just use a single default channel map.
  Cisco never implemented TR Config Files on the SARA App Server, so if a site needs to use a TR Config File, that is entirely the responsibility of the 3rd-party vendor, e.g., ATG publishes the TR Config File on BFS from their Mystro Application Server (MAS).
  Subsription packages go on the Cable Card in the TiVo.
  The TA only needs the brick package and the SDV package.
  With a TA connected to a TiVo, the channel map no longer comes from the cable card but from the TA.

## Slide 24: Dan Hisaw
ENGINEER.CUSTOMER SUPPORT