## Slide 1: Introduction to the Cisco CMTS
Eric Bautista
erbautis@cisco.com
Notes: <number>

## Slide 2: Agenda
Role of a CMTS in a cable Multiple System Operator (MSO) network
Brief overview of Cisco’s CMTS product family
uBR7200 product line overview
uBR10K product line overview
Basic configuration and show commands
Q& A
Skill Based Objective
Given basic information and “show” commands from a Cisco CMTS, the learner will be able to identify what platform and modules are being used. They will also be able to describe the HFC topology and describe the current state of the cable interfaces.
Notes: MSO stands for Multiple System Operator. MSO is the industry term for "cable company". Each cable TV installation serving a community is known as a "cable system", and the operator of the system is called the "system operator". Most system operators run cable systems in more than one community. Therefore, the vast majority of them are Multiple System Operators.
<number>

## Slide 3: Learner Objectives
Name
Department
What would you like to get out of this lesson?
Notes: Before we move on, I’d like to have everyone introduce themselves, give us the department you work for and answer the question.
Who’d like to get us started?
Who’s next?
(don’t say “anybody else?”)
Sangeetha, Brian, Brandon, Dave, Eric, Andrzej
<number>

## Slide 4: Role of a CMTS
Notes: <number>

## Slide 5: What is a CMTS
CMTS stands for Cable Modem Termination System
The CMTS is a provider edge system which interfaces the RF cable plant side to the provider IP core network
CMTS’s allow Service Providers to offer broadband High Speed Data (HSD) and other IP based services to the end subscribers connected to their cable network – including Voice and Video.
DOCSIS (Data Over Cable Service Interface Specification): Defines interface requirements for cable modems involved in high-speed data delivery over cable's hybrid fiber-coaxial plant.
Notes: Network Diagram in next slide.
<number>

## Slide 6: Cable Broadband Architecture
CM
CM
CM
CM
CM
CM
CM
CM
CMTS
CMTS
CMTS
Access Network
CM
CM
Service Provider IP Core Network
Core Network
Operator administered
DOCSIS
CM
CPE
Headend
Internet
SP Core
Notes: The CMTS is a Cisco Universal Broadband Router (uBR) with features that enable it to communicate with a Hybrid Fiber Coaxial (HFC) Cable network via a Cisco MCxx cable modem card. Cisco MCxx cable modem cards allow you to connect cable modems on the HFC network to a Cisco uBR7200, uBR7100 or a uBR10k in a Community Antenna Television (CATV) headend facility. The modem card provides the interface between the Cisco uBR protocol control information (PCI) bus and the radio frequency (RF) signal on the DOCSIS HFC network.
Data-over-Cable Service Interface Specifications (DOCSIS) defines technical specifications for equipment at both subscriber locations and cable operators' headends. Adoption of DOCSIS accelerates the deployment of data-over-cable services and will ensure interoperability of equipment throughout system operators' infrastructures.
http://www.cablelabs.com/cablemodem/specifications/index.html
<number>

## Slide 7: Functions performed by a CMTS
Provides network side interfaces ( i.e. Gigabit Ethernet ) to the provider IP network
Provides RF side interfaces to the cable plant.
A “legacy” RF side interface consists of one downstream channel and multiple upstream channels
  Downstream channels carry traffic from the CMTS to the cable modems
  Upstream channels carry traffic from the cable modems to the CMTS
CMTS performs switching / routing functionality between the RF side and network side interfaces
  This switching/routing function is very similar to that of a typical IP router
Notes: The CMTS is a Cisco Universal Broadband Router (uBR) with features that enable it to communicate with a Hybrid Fiber Coaxial (HFC) Cable network via a Cisco MCxx cable modem card. Cisco MCxx cable modem cards allow you to connect cable modems on the HFC network to a Cisco uBR7200, uBR7100 or a uBR10k in a Community Antenna Television (CATV) headend facility. The modem card provides the interface between the Cisco uBR protocol control information (PCI) bus and the radio frequency (RF) signal on the DOCSIS HFC network.
Data-over-Cable Service Interface Specifications (DOCSIS) defines technical specifications for equipment at both subscriber locations and cable operators' headends. Adoption of DOCSIS accelerates the deployment of data-over-cable services and will ensure interoperability of equipment throughout system operators' infrastructures.
<number>

## Slide 8: Why is it important to describe how a CMTS is set-up?
You can better isolate what may be causing the issue.
You can better collaborate with the WW-CABLE engineers.
Customers will be impressed.
End-to-end lab recreate
Test for understanding
What does CMTS stand for?
What is the name of the set of specifications that define the requirements for cable modems and hybrid fiber-coaxial plants?
True or False: Downstream channels carry traffic from the CMTS to the cable modems.
Notes: You can better isolate what may be causing the issue. – Ask better question. Eliminate non-factors
You can better collaborate with the WW-CABLE engineers. – Expedite resolution.
Customers will be impressed. - We are getting into SOLUTIONS BASED support. If you’re on a bridge with video, network, provisioning, teams, etc. you can communicate with them more thoroughly.
<number>

## Slide 9: Cisco CMTS Products
Cisco uBR7225VXR Universal Broadband Routers
  Mid to Entry level CMTS
  Up to 16 upstream and 16 downstream ports in a 2-RU form factor
  Supports up to 5,000 subscribers
Cisco uBR7246VXR Series Universal Broadband Routers
  High performance, communications-grade CMTS
  Up to 32 upstream and 32 downstream ports in a 6-RU form factor
  Supports up to 10,000 subscribers
Cisco uBR10000 Series Universal Broadband Routers
  Highest performance and port capacity
  Up to 480 upstream and 576 downstream ports in a
  Supports up to 64,000 subscribers
Notes: http://www.cisco.com/en/US/products/ps8474/index.html
http://www.cisco.com/en/US/prod/collateral/video/ps8806/ps5684/ps2217/product_data_sheet09186a0080092234_ps2211_Products_Data_Sheet.html
http://www.cisco.com/en/US/partner/docs/cable/cmts/ubr10012/installation/guide/u10kov.html
uBR10k 64,000 subscribers  This is for reference only. The total number of subscribers for specific systems might vary depending on whether high availability is deployed, network or service loading, traffic, features deployed, and other parameters. A high availability N+1 enabled system with more than 50,000 subscribers is not recommended.
<number>

## Slide 10
Cisco uBR7225 VXR Overview
Notes: <number>

## Slide 11: uBR7225VXR
1 | Gigabit Ethernet 0/1 | 5 | Console port
2 | Gigabit Ethernet 0/2 | 6 | Auxiliary port
3 | Gigabit Ethernet 0/3 | 7 | AC-input power supply 2
4 | Network processing engine | 8 | AC-input power supply 1
Notes: Pizza Box
16U in slot 1
28U in slot 2
4US per 1 DS general guideline
<number>

## Slide 12: Cisco uBR7225VXR CMTS
uBR7225VXR CMTS chassis has two slots for Cable interface line cards and one slot for Network Processing Engine (NPE).
Chassis mid-plane bridges the PCI buses from cable interface line cards to the Network Processing Engine (NPE-G1 & NPE-G2)
Mid-plane supports an aggregate bandwidth of 600 Mbps
Supports both DOCSIS & Euro-DOCSIS operation
It supports the following cable line cards:
  UBR-MC16U, UBR-MC28U and uBR-MC88V
  Cisco uBR7225VXR E-28U BPE (compatible with the uBR7225VXR chassis only )
  Cisco uBR7225VXR E-16U BPE (compatible with the uBR7225VXR chassis only )
Notes: http://www.cisco.com/en/US/prod/collateral/modules/ps4969/product_data_sheet0900aecd8012a71e.html
http://www.cisco.com/en/US/prod/collateral/modules/ps4969/ps10737/data_sheet_c78-570335.html
http://www.cisco.com/en/US/prod/collateral/modules/ps4969/product_data_sheet0900aecd806b8f35.html
<number>

## Slide 13: Network Processing Engine for uBR7225VXR
NPE performs the following system management functions:
  Sending and receiving routing protocol updates
  Managing tables, caches, and buffers
  Monitoring interface and environmental status
  Providing Simple Network Management Protocol (SNMP) management and console/Telnet interface
  Accounting and switching of data traffic
Part Numbers:
  uBR7200-NPE-G1
  uBR7200-NPE-G2
Notes: http://www.cisco.com/en/US/products/hw/modules/ps4917/ps4951/index.html
http://www.cisco.com/en/US/products/ps8591/index.html
<number>

## Slide 14: Cable line Cards for uBR7225 VXR
UBR-MC16U, UBR-MC28U and uBR-MC88V
1X6 cards support a single cable mac domain with one downstream and six upstream channels
2X8 cards support two cable mac domains each with one downstream and four upstream channels
8x8 cards support two cable mac domains which can be configured with various combinations of downstream and upstream channels.
Notes: http://www.cisco.com/en/US/prod/collateral/modules/ps4969/product_data_sheet0900aecd806b8f35.html
>>>>MAC DOMAIN:
A “legacy” RF side interface consists of one downstream channel and multiple upstream channels
  Downstream channels carry traffic from the CMTS to the cable modems
  Upstream channels carry traffic from the cable modems to the CMTS
<number>

## Slide 15
Cisco uBR7246 VXR Overview
Notes: <number>

## Slide 16: uBR7246VXR
Chassis based mid-range CMTS which supports up to 10,000 subscribers
Chassis supports a total of four cable line cards
Supports two port adapters for IP core side connectivity
Supports NPE-G2 and NPE-G1 & NPE-400 (Older versions of the software supported NPE-225 as well)
Optional I/O controller (Not a requirement for NPE-G1 &G2)
One optional cable clock card

## Slide 17: uBR7246VXR
1 | Internal fans | 9 | Auxiliary port
2 | Clock card | 10 | Optional Fast Ethernet port (M11 and RJ-45 receptacles)
3 | Fan tray handle | 11 | PCMCIA slots
4 | Captive installation screws (line cards) | 12 | AC plug1
5 | Cable interface line cards | 13 | Power switch
6 | Port adapters | 14 | Power supply handle
7 | I/O controller | 15 | AC-input power supply
8 | Console port | 16 | Network processing engine (NPE)
Notes: http://www.cisco.com/en/US/partner/prod/collateral/video/ps8806/ps5684/ps2217/product_data_sheet09186a0080092234.html
<number>

## Slide 18: Cable Line Cards for uBR7246 VXR
UBR-MC16U/X : 1 DS port and 6 US ports. One 1X6 RF mac-domain. Built In or external upconverter.
UBR-MC28U/X : 2 DS ports and 8 US ports. Two 1X4 RF mac-domains. Built in or external upconverters.
uBR-MC88V : 2 DS ports and 8 US ports. 2 RF mac-domains.
Older Cable Cards : MC16C, MC16S, MC16E, MC11C, MC14C etc.
Notes: X = External upconverter needed.
IF = intermediate frequency
The Cisco uBR-MC16U/X card has one downstream port and six upstream ports, organized into a single DOCSIS MAC domain. There are two versions, the Cisco uBR-MC16U and the Cisco uBR-MC16X, which are identical except for the type of upconverter that the downstream ports use:
•Cisco UBR-MC16U card—Each downstream port includes an onboard integrated upconverter that generates an RF signal suitable for connection to a combiner and transmission on the coaxial cable network, without the need for any external upconverters.
•Cisco uBR-MC16X card—The downstreams on this card do not include integrated upconverters. Instead, the downstream ports generate an IF signal that must be converted through an external upconverter before transmission on the cable network. This allows the Cisco uBR-MC16X card to easily replace existing line card installations that currently use external upconverters.
End of Sale, Engineering, and Life Notices
http://www.cisco.com/en/US/prod/collateral/modules/ps4302/prod_end-of-life_notice0900aecd8050b7ec.html
http://www.cisco.com/en/US/partner/prod/collateral/modules/ps4302/prod_end-of-life_notice0900aecd801e8a41_ps2217_Products_End-of-Life_Notice.html
http://www.cisco.com/en/US/partner/products/hw/cable/ps2217/prod_eol_notice09186a008032d4ba.html
Cisco uBR7200 Series Cable Interface Line Card Hardware Installation Guide
http://www.cisco.com/en/US/partner/docs/interfaces_modules/cable/line_cards/installation/guide/mcxxfru.html#wp1074200
The Cisco uBR-MC88V cable interface line card has eight RF upstream (US) and two downstream (DS) physical connectors. Each downstream physical connector includes four downstream channels. The Cisco uBR-MC88V line card supports two cable interfaces (MAC domains), and the downstream and upstream channels are dynamically associated with any of these MAC domains.
<number>

## Slide 19
Cisco uBR10012 Overview
Notes: <number>

## Slide 20: uBR10K series – A new class of CMTS
DOCSIS 1.1 & DOCSIS 2.0 Qualified
Optimized for aggregation
  Increases intelligence at edge of the network
  Balanced system, maximizes useful capacity where needed
Future Scalability
  Passive point-point Midplane
  Fully upgradeable processors, WAN interfaces, RF cards
  Have overcome all potential bottlenecks
Notes: Flagship
http://www.cisco.com/en/US/partner/products/hw/cable/ps2209/prod_installation_guides_list.html
<number>

## Slide 21
Display Module
High Capacity WAN Interfaces, Replaceable On-line
Redundant DC or AC* Power Supplies
Redundant Processor Modules with Route Processor Redundancy (RPR) Automatic Failover Option
Redundant Interface to External Stratum 1 Clock Reference (GPS or BITS)
Flexible DOCSIS Card support with N+1 Redundancy
Modular, variable speed blower assembly
uBR10012 Components
Notes: N+1 redundancy available.. Where Slot 5/1 is the designated protect linecard.
<number>

## Slide 22: Chassis Slot Numbering
1 | Fan assembly module | 3 | Two PRE modules
2 | LCD module | 4 | Two DC PEM modules
Notes: http://www.cisco.com/en/US/partner/docs/cable/cmts/ubr10012/installation/guide/u10kov.html
<number>

## Slide 23
Forwarding
Processor
Route
Processor
PRE
RF
Linecards
LAN / WAN
Control Plane
TCC+
Stratum 3 Clocks,
Synched to Stratum 1
System Clocks & Resets
Data Plane
Local “switch fabric”
uBR10012 - Architecture
10B2
10B2
800Mbps x 2 x 8
1.6Gbps x2 x4
FE

## Slide 24: uBR10K System Architecture
Primary PRE
Secondary PRE
Cable Line
Card
CLC
CLC
Spumoni Jacket Card
(Full Height, Double Width)
SPA
SPA
SPA
SPA
SPI4.2
SPAbus
IronBus
InterProcessor Ethernet
BackPlane Ethernet
█ Data Plane
▒ Control Plane
█ Timing Plane
active -DTCC+
stby - DTCC+
CLC Ethernet
Notes: <number>
SPA’s

## Slide 25: uBR10k Performance Routing Engines
The PRE module is a single-slot module used with the Cisco uBR10012 universal broadband routers.
The PRE performs all Layer 2 and Layer 3 packet routing and forwarding.
PRE modules support redundant operation when installing two PRE modules in a Cisco uBR10012 chassis. If the active PRE fails, the standby PRE automatically takes over operation of the chassis.
Part Numbers:
  ESR-PRE1
  ESR-PRE2
  ESR-PRE4
Notes: http://www.cisco.com/en/US/partner/docs/interfaces_modules/cable/performance_routing_engine/installation/guide/pre5096.html
<number>

## Slide 26: PRE4 Faceplate
Figure 1 Performance Routing Engine Front Panel
1 | Ejector Levers | 6 | ACO (Alarm Cut-off Button)
2 | Console and Auxiliary Ports | 7 | CompactFlash Slot, Disk0
3 | Network Management Ethernet (NME) Port | 8 | Slot0 (Disk0) LED
4 | NME Activity and Link LEDs /Push-button reset | 9 | Status, Fail LEDs
5 | Alarms: Critical, Major, Minor | 10 | Building Internal Timing Source (BITS) LED (c10k only)
Notes: <number>
http://www.cisco.com/en/US/prod/collateral/video/ps8806/ps5684/ps2209/end_of_life_notice_c51-669670.html
http://www.cisco.com/en/US/prod/collateral/routers/ps133/data_sheet_c78-460875.html
The Cisco 10000 Series PRE4 delivers both scalability improvements and new features:
• Provides up to 10 million packets per second (mpps) of processing power for increased throughput
• Delivers Hierarchal Queuing Framework (HQF) for up to three levels of service granularity
• Supports increased bandwidth through link bonding connections between the PRE4 and Cisco 10000 Series SPA Interface Processor (SIP)-600
– 11.2 Gbps transmit and receive (full duplex) to any SIP (total bandwidth distributed across installed shared port adapters [SPAs])
– 2.8 Gbps transmit and receive (full duplex) to each full-height line card
– 1.4 Gbps transmit and receive (full duplex) to each half-height line card
• Includes 800-MHz route processor with 4 GB ECC protected DRAM for new features and scalability improvements
• Delivers enhanced storage options for larger and more complex configurations
– 14 MB nonvolatile RAM (NVRAM)
– 128 MB Compact Flash - fixed internal memory
– 512 MB or 1 GB Compact Flash - front panel removable memory
• Uses Cisco patented PXF technology to provide maximum IP service flexibility without performance impact
• Supports processor redundancy, helping enable 99.999-percent network uptime
• Support for Building Integrated Timing Supply (BITS) interface, a component of the Cisco 10000 Series BITS architecture that enables network service synchronization

## Slide 27: PRE4 Faceplate
Figure 1 Performance Routing Engine Front Panel
PRE4 Connectors
The front panel on the PRE4 contains three ports with RJ-45 connectors.
Console port (CONSOLE)
  This asynchronous serial port is used to connect a terminal to the PRE4 for local administrative access.
Auxiliary port (AUX)
  This asynchronous serial port is used to connect a modem to the PRE4 for remote administrative access.
NME Port
  This Ethernet port is used to connect the PRE4 to a Fast Ethernet port. To be used for management purposes, only.
CompactFlash Card Slot
The external CompactFlash slot can store the Cisco IOS image or a system configuration file on a flash memory card. The system can also boot from the software stored on the flash memory card.
Notes: <number>
1 – Ejector Levers
2 – Console and Aux ports
3 – NME port
4 – NME activity and link LEDs
5 – Alarms

## Slide 28: Cable line Cards for uBR10k
UBR10-5x20S-D, UBR10-5x20U-D, UBR10-5x20H-D
  Five downstream (DS) ports and twenty upstream (US) ports.
  5x20 cards support up to five cable MAC domains.
  Typically each mac domain consists of 1 downstream and 4 upstream channels.
UBR-MC20X20V
  Five downstream (DS) ports and twenty upstream (US) ports
  The line card supports five cable MAC domains, and the 20 DS and 20 US channels are dynamically associated with any of these five MAC domains.
  Each of the US ports support either two-frequency stacked US channels across ten ports or a single US channel across twenty ports.
  Each of the DS ports supports four-frequency stacked channels across five ports.
uBR-MC3GX60V
  72 downstream (DS) and 60 upstream (US) channels
  The line card supports 15 cable MAC domains.
  The DS and US channels can be associated with any of these 15 MAC domains.
  Each MAC domain supports a maximum of 32 DS and 8 US channels.\
Notes: http://www.cisco.com/en/US/partner/products/hw/modules/ps4969/products_data_sheets_list.html
http://www.cisco.com/en/US/docs/interfaces_modules/cable/broadband_processing_engines/ubr_mc20x20v/installation/guide/mc20x20v_hig.html
http://www.cisco.com/en/US/products/hw/cable/ps2209/prod_installation_guides_list.html
uBR-MC3GX60V
<number>

## Slide 29: MC5X20S/U/H Cable Line Card
DS ports 0 - 4
US ports 0 - 9
US ports 10 - 19
Notes:   20x20 looks the same, but each of the DS ports is capable of supporting four-frequency stacked channels across the five physical DS ports.
<number>

## Slide 30: uBR-MC3GX60V Cable Line Card
The Cisco uBR-MC3GX60V cable interface line card has six Gigabit Ethernet (GE) interface ports organized into three pairs for DS connectivity. Each pair supports 1+1 redundancy
The GE interfaces connect to an external Edge Quadrature Amplitude Modulation (EQAM) device.
Notes: http://www.cisco.com/en/US/partner/prod/collateral/modules/ps4969/ps11291/data_sheet_c78-642540.html
EQAM: RFGW-1, RFGW-10, Harmonic NSG
Licensing:
http://www.cisco.com/en/US/docs/cable/cmts/license/cmts_swact.html
<number>

## Slide 31: uBR10012 Router Shared Port Adapters
SPA-24XDS-SFP: Cisco Wideband SPA
  The Cisco Wideband SPA is used for downstream data traffic only.
  One ACTIVE and one PROTECT Gigabit Ethernet port.
  Used to send traffic to the external edge QAM device.
SPA-5X1GE-V2: 5-Port Gigabit Ethernet SPA
SPA-1X10GE-L-V2: 1-Port 10-Gigabit Ethernet SPA
Notes: http://www.cisco.com/en/US/docs/interfaces_modules/shared_port_adapters/install_upgrade/uBR10012/ubrsov.html
http://www.cisco.com/en/US/partner/prod/collateral/modules/ps6267/product_data_sheet0900aecd804b424e_ps2209_Products_Data_Sheet.html
M-CMTS vs. I-CMTS
DEPI - Downstream External PHY Interface
<number>

## Slide 32: Review
How many upstreams and downstreams does a UBR10-5X20U-D linecard support? On what platform?
What Network Processing Engines can be used on a uBR7225 platform?
Notes: <number>

## Slide 33
Basic Configuration
and “show” Commands
Every online cable modem must lock onto a downstream carrier and upstream carrier in order to have bi-directional communication.
The coaxial cable which reaches the modem must be carrying both US and DS frequencies.
A MAC-Domain is one Downstream and at least one Upstream
Notes: 55-999 MHz, edge-to-edge
<number>

## Slide 34: Downstream Frequency
CMTS#show run interface cable 8/0/0
interface Cable8/0/0 cable downstream annex B cable downstream modulation 256qam cable downstream interleave-depth 32 cable downstream frequency 687000000 cable downstream channel-id 0 cable downstream rf-shutdown
Most Cable Line Cards (CLC) now have a built-in upconvertor. Exceptions are the older cards such as MC16C and MC28C.
Relevant Commands: show controller cable <X/Y/Z> downstream show controller cable <X/Y/Z> show running interface cable <X/Y/Z>
Notes: <number>

## Slide 35: Downstream Frequency
CMTS#show controllers cable 8/0/0 downstream Cable8/0/0 Downstream is up Frequency 687.0000 MHz, Channel Width 6 MHz, 256-QAM, Symbol Rate 5.360537 Msps FEC ITU-T J.83 Annex B, R/S Interleave I=32, J=4 Downstream channel ID: 0 CMTS#show controllers cable 8/0/0 | begin Upconverter Upconverter: vcom Cable8/0/0 Upconverter is Enabled Output is Enabled Model: 74-3153-02 Serial Number: 0WAV084000UV CLEI Code: FFFFFFFFFF HW Rev: PC2D0109 SW Rev: 203, NVRAM Rev: 021 ECI number FFFFFF Downstream Frequency 687.0000 MHz RF Power 61.0 dB
Relevant Commands: show controller cable <X/Y/Z> downstream show controller cable <X/Y/Z> show running interface cable <X/Y/Z>
DS ports frequency range: 55-999 MHz
(varies by linecard)
Notes: <number>

## Slide 36: Downstream Modulation
CMTS#show run interface cable 8/0/0
interface Cable8/0/0 cable downstream annex B cable downstream modulation 256qam cable downstream interleave-depth 32 cable downstream frequency 687000000 cable downstream channel-id 0 cable downstream rf-shutdown
The downstream modulation should be set. Many MSO’s, especially if they support digital cable, now operate at 256 QAM.
Relevant Commands: show controller cable <X/Y/Z> downstream show controller cable <X/Y/Z> show running interface cable <X/Y/Z>
Notes: <number>

## Slide 37: Downstream Modulation
CMTS#show controllers cable 8/0/0 downstream Cable8/0/0 Downstream is up Frequency 687.0000 MHz, Channel Width 6 MHz, 256-QAM, Symbol Rate 5.360537 Msps FEC ITU-T J.83 Annex B, R/S Interleave I=32, J=4 Downstream channel ID: 0 CMTS#show controllers cable 8/0/0 | begin Upconverter Upconverter: vcom Cable8/0/0 Upconverter is Enabled Output is Enabled Model: 74-3153-02 Serial Number: 0WAV084000UV CLEI Code: FFFFFFFFFF HW Rev: PC2D0109 SW Rev: 203, NVRAM Rev: 021 ECI number FFFFFF Downstream Frequency 687.0000 MHz RF Power 61.0 dB
Relevant Commands: show controller cable <X/Y/Z> downstream show controller cable <X/Y/Z> show running interface cable <X/Y/Z>
Notes: <number>

## Slide 38: Downstream Port Enable
CMTS#show run interface cable 8/0/0
interface Cable8/0/0 cable downstream annex B cable downstream modulation 256qam cable downstream interleave-depth 32 cable downstream frequency 687000000 cable downstream channel-id 0 no cable downstream rf-shutdown cable downstream rf-power 61
The default downstream configuration has RF output disabled. Enable this explicitly.
Relevant Commands: show controller cable <X/Y/Z> downstream show running interface cable <X/Y/Z>
Notes: <number>

## Slide 39: Downstream Port Enable
CMTS#show controllers cable 8/0/0 | begin Upconverter Upconverter: vcom Cable8/0/0 Upconverter is Disabled Output is Disabled Model: 74-3153-02 Serial Number: 0WAV084000UV CLEI Code: FFFFFFFFFF HW Rev: PC2D0109 SW Rev: 203, NVRAM Rev: 021 ECI number FFFFFF Downstream Frequency 687.0000 MHz RF Power Disabled CMTS#conf t Enter configuration commands, one per line. End with CNTL/Z. CMTS(config)#int c8/0/0 CMTS(config-if)#no cable downstream rf-shutdown CMTS(config-if)# SLOT 8/0: Apr 1 16:36:41.102 UTC: %UPCONV-5-UPDOWN: interface Cable8/0/0 upconverter output changed to Up CMTS(config-if)#^Z CMTS#show controllers cable 8/0/0 | begin Upconverter Upconverter: vcom Cable8/0/0 Upconverter is Enabled Output is Enabled Model: 74-3153-02 Serial Number: 0WAV084000UV CLEI Code: FFFFFFFFFF HW Rev: PC2D0109 SW Rev: 203, NVRAM Rev: 021 ECI number FFFFFF Downstream Frequency 687.0000 MHz RF Power 55.0 dB
Relevant Commands: show controller cable <X/Y/Z> show running interface cable <X/Y/Z>
Notes: <number>

## Slide 40: Downstream RF power output
CMTS#show run interface cable 8/0/0
interface Cable8/0/0 cable downstream annex B cable downstream modulation 256qam cable downstream interleave-depth 32 cable downstream frequency 687000000 cable downstream channel-id 0 cable downstream rf-shutdown cable downstream rf-power 61
With the exception of older legacy cards, CLC’s produce RF output which should be set according to a plant’s power budget.
Note some CLC’s only produce IF output and need an external upconvertor.
Relevant Commands: show controller cable <X/Y/Z> show running interface cable <X/Y/Z>
Notes: <number>
IF = Intermediate Frequency

## Slide 41: Downstream RF power output
CMTS#show controllers cable 8/0/0 | begin Upconverter Upconverter: vcom Cable8/0/0 Upconverter is Enabled Output is Enabled Model: 74-3153-02 Serial Number: 0WAV084000UV CLEI Code: FFFFFFFFFF HW Rev: PC2D0109 SW Rev: 203, NVRAM Rev: 021 ECI number FFFFFF Downstream Frequency 687.0000 MHz RF Power 61.0 dB
Relevant Commands: show controller cable <X/Y/Z> show running interface cable <X/Y/Z>
Notes: <number>

## Slide 42: Upstream Frequency
CMTS#show run interface cable 8/0/0
interface Cable8/0/0 cable upstream 0 frequency 24000000 cable upstream 0 channel-width 3200000 3200000 cable upstream 0 minislot-size 4 cable upstream 0 modulation-profile 21 cable upstream 0 shutdown
Relevant Commands: show controller cable <X/Y/Z> upstream <W> show running interface cable <X/Y/Z>
US ports frequency range: 5-85 MHz
(varies by linecard)
Notes: <number>

## Slide 43: Upstream Frequency
CMTS1#show controller cable 8/0/0 upstream 0 Cable8/0/0 Upstream 0 is administratively down Frequency 24.000 MHz, Channel Width 3.200 MHz, 64-QAM Symbol Rate 2.560 Msps This upstream is mapped to physical port 0 Spectrum Group is overridden MER(SNR) - Unknown - no modems online. Nominal Input Power Level 1 dBmV, Tx Timing Offset 0 Ranging Backoff Start 3, Ranging Backoff End 6 Ranging Insertion Interval automatic (60 ms)
Relevant Commands: show controller cable <X/Y/Z> upstream <W> show running interface cable <X/Y/Z>
Notes: <number>

## Slide 44: Upstream Channel Width
CMTS#show run interface cable 8/0/0
interface Cable8/0/0 cable upstream 0 frequency 24000000 cable upstream 0 channel-width 3200000 3200000 cable upstream 0 minislot-size 4 cable upstream 0 modulation-profile 21 cable upstream 0 shutdown
Set the channel width.
Note that the CMTS will allow frequencies to overlap, so ensure that there is adequate separation between frequency bands.
The example below shows a channel width of 3.2MHz.
Relevant Commands: show controller cable <X/Y/Z> upstream <W> show running interface cable <X/Y/Z>
Notes: <number>

## Slide 45: Upstream Channel Width
CMTS1#show controller cable 8/0/0 upstream 0 Cable8/0/0 Upstream 0 is administratively down Frequency 24.000 MHz, Channel Width 3.200 MHz, 64-QAM Symbol Rate 2.560 Msps This upstream is mapped to physical port 0 Spectrum Group is overridden MER(SNR) - Unknown - no modems online. Nominal Input Power Level 1 dBmV, Tx Timing Offset 0 Ranging Backoff Start 3, Ranging Backoff End 6 Ranging Insertion Interval automatic (60 ms)
Relevant Commands: show controller cable <X/Y/Z> upstream <W> show running interface cable <X/Y/Z>
Notes: <number>

## Slide 46: Upstream Port Enable
interface Cable8/0/0 cable upstream 0 frequency 24000000 cable upstream 0 channel-width 3200000 3200000 cable upstream 0 minislot-size 4 cable upstream 0 modulation-profile 21 no cable upstream 0 shutdown
The default upstream configuration has the port shutdown.
Enable this explicitly.
Relevant Commands: show controller cable <X/Y/Z> upstream <W> show running interface cable <X/Y/Z>
Notes: <number>

## Slide 47: Upstream Port Enable
CMTS1#show controller cable 8/0/0 upstream 0 Cable8/0/0 Upstream 0 is administratively down Frequency 24.000 MHz, Channel Width 3.200 MHz, 64-QAM Symbol Rate 2.560 Msps This upstream is mapped to physical port 0 Spectrum Group is overridden MER(SNR) - Unknown - no modems online. CMTS1#conf term Enter configuration commands, one per line. End with CNTL/Z. CMTS1(config)#int c8/0/0 CMTS(config-if)#no cable upstream 0 shutdown 523869: *Apr 1 16:51:00.545 UTC: %UBR10000-5-UPDOWN: Interface Cable8/0/0 U0, changed state to up 523870: *Apr 1 16:51:00.545 UTC: %ALARM-6-ENTITY_INFO: CLEAR INFO Cable8/0-US0 Physical Port Administrative State Down 523871: *Apr 1 16:51:00.545 UTC: %SNMP-5-LINK_UP: LinkUp:Interface Cable8/0/0-upstream0 changed state to up CMTS(config-if)#^Z CMTS1#show controller cable 8/0/0 upstream 0 Cable8/0/0 Upstream 0 is up Frequency 24.000 MHz, Channel Width 3.200 MHz, 64-QAM Symbol Rate 2.560 Msps This upstream is mapped to physical port 0 Spectrum Group is overridden US phy MER(SNR)_estimate for good packets - 34.398 dB
Relevant Commands: show controller cable <X/Y/Z> upstream <W> show running interface cable <X/Y/Z>
Notes: <number>

## Slide 48: Cable Modems
CMTS1#show cable modem 0023.a279.1d7c
D
MAC Address IP Address I/F MAC Prim RxPwr Timing Num I
State Sid (dBmv) Offset CPE P
0023.a279.1d7c 10.1.1.2 C7/1/0/U0 online(pt) 6 -0.50 1441 0 N
CMTS1#show cable modem summary total
Interface Cable Modem Description
Total Reg Oper Unreg Offline Wideband initRC initD initIO initO
C6/0/0/U0 3 3 3 0 0 1 0 0 0 0
C6/0/0/U1 1 1 1 0 0 0 0 0 0 0
C7/1/0/U0 4 4 4 0 0 3 0 0 0 0
Total: 8 8 8 0 0 4 0 0 0 0
Relevant Commands:
show cable modem <mac> show cable modem <mac> verbose
show cable modem <mac> cpe show cable modem summary total
Notes: <number>
Note “Offline” and “Unreg” sections for outage situations.
Understanding show cable modem Command States:
http://www.cisco.com/en/US/tech/tk86/tk168/technologies_tech_note09186a00801494b8.shtml

## Slide 49: show version
CMTS1#show version
Cisco IOS Software, 10000 Software (UBR10K4-K9P6U2-M), Version 12.2(33)SCF1, RELEASE SOFTWARE (fc1)
Technical Support: http://www.cisco.com/techsupport
Copyright (c) 1986-2011 by Cisco Systems, Inc.
Compiled Fri 30-Sep-11 18:16 by prod_rel_team
ROM: System Bootstrap, Version 12.2(20071113:194412) [shalpin-rom-1_2 101], DEVELOPMENT SOFTWARE
CMTS1 uptime is 3 days, 15 hours, 12 minutes
Uptime for this control processor is 3 days, 15 hours, 12 minutes
System returned to ROM by reload at 07:52:34 UTC Thu Apr 5 2012
System image file is "disk0:ubr10k4-k9p6u2-mz.122-33.SCF1.bin"
Last reload type: Normal Reload
Last reload reason: Reload command
Relevant Commands: show version
Notes: <number>

## Slide 50: show version (cont.)
Cisco uBR10000 (PRE4-RP) processor with 2588671K/163839K bytes of memory.
Processor board ID SPE10280C6C
SB-1 CPU at 800Mhz, Implementation 0x410, Rev 5.0, 512KB L2 Cache
Backplane version 1.1, 8 slot
Last reset from software reset
PXF processor tmc0 is running.
PXF processor tmc1 is running.
PXF processor tmc2 is running.
PXF processor tmc3 is running.
2 DTCC card(s)
1 Jacket card(s): 2 SPA card(s)
1 FastEthernet interface
40 Cable Modem interfaces
7039K bytes of non-volatile configuration memory.
125184K bytes of ATA compact flash in bootflash (Sector size 512 bytes).
990864K bytes of ATA compact flash in disk0 (Sector size 512 bytes).
Standby is up
Standby has 2752512K bytes of memory
Configuration register is 0x2102
Relevant Commands: show version
Notes: <number>

## Slide 51: Facility alarms
CMTS1#sh facility-alarm status
Thresholds:
Intake minor 41 major 51 critical 73
Outlet minor 48 major 58 critical 85
System Totals Critical: 1 Major: 0 Minor: 0
Source Severity ACO Description [Index]
------ -------- --- -------------------
slot 4/0 INFO NORMAL Unsupported card type OIR Alarm - subslot 0 [4]
SFP container 1/0/0 CRITICAL NORMAL SFP Missing Alarm [0]
Cable5/0-US2 INFO NORMAL Physical Port Administrative State Down [1]
Cable5/0-US3 INFO NORMAL Physical Port Administrative State Down [1]
Cable5/0-US4 INFO NORMAL Physical Port Administrative State Down [1]
Relevant Commands: show facility-alarm status show logging
Notes: <number>

## Slide 52: Inventory
CMTS1#show inventory
NAME: "Chassis", DESCR: "uBR10000 chassis"
PID: UBR10012 , VID: , SN: SPE10280C6C
NAME: "RP A", DESCR: "Performance Routing Engine"
PID: ESR-PRE4 , VID: V01 , SN: CAT1203F0AB
NAME: "SPA bay 1/0", DESCR: "WIDEBAND DOCSIS SPA"
PID: SPA-24XDS-SFP , VID: V01, SN: CAT10385B64
NAME: "module 5/1", DESCR: "MC520U_D_connector"
PID: UBR10-MC5X20U-D , VID: V02 , SN: CAT111958UZ
NAME: "module 6/0", DESCR: "MC20X20 I-CMTS 20DSX20US CLC"
PID: UBR-MC20X20V , VID: V01 , SN: CAT1339E06Q
NAME: "module 7/0", DESCR: "MC20X20 I-CMTS 20DSX20US CLC"
PID: UBR-MC20X20V , VID: V01 , SN: CAT1340E01Q
NAME: "module 7/1", DESCR: "MC3G60 M-CMTS 3GE 72DSX60US CLC"
PID: UBR-MC3GX60V , VID: V01 , SN: CAT1441E125
Relevant Commands: show inventory show diag
Notes: <number>
<snip>

## Slide 53: Test For Understanding
Relevance
What command will display the platform and IOS version in use?
What command(s) can you check to verify the downstream frequency that is configured?
  In what situations do you think you will be able to use this?
  Learner objectives.
Relevance
Notes: <number>