## Slide 1
Cisco Support Community
(SP Mobility)
-By Ruchi Shroti
Recovering Console Password
for ASR5000/5500

## Slide 2
Agenda
Pre-requisites.
Problem Reproduction.
Solution Overview.
Solution Verification.

## Slide 3
Pre -requisites
A working serial cable provided by Cisco to connect to the ASR5000 or ASR5500 console port.
HyperTerminal application should be installed in the workstation used to connect to the ASR console.
Latest configuration of the ASR should be saved on the flash. Any unsaved configuration will be lost during this activity.

## Slide 4
Problem Reproduction
Follow the instructions below to connect to the console port.
1.Connect the RJ-45 end of the cable to the port labeled Console.
2.Connect the DB-9 end of the cable to the serial port on the workstation/laptop.
3.Go to computer management device managerports to get the proper COM port (This is a windows machine)

## Slide 5
Note : Remember this COM Port it will be required during login from HyperTerminal or putty.

## Slide 6
Now click on Hyper term application follow below steps
Give any name to the connection and press ok
Use the COM same as shown in last slide
Set the properties as saved above and click on OK you will get console login prompt (See next slide)

## Slide 7
Try to login with existing credential it will give Login incorrect error

## Slide 8
Solution To Recover the Console Password.
Initiate a Reboot
A reload can be initiated in one of two ways:
- Power cycle the chassis
Turn the circuit breakers on the power filter units (PFUs) Off (0) and then On (I).
- Execute a reload command
[local]asr5000# reload -noconfirm
The boot sequence displays messages on the terminal as it steps through its processes.

## Slide 9
1. You will see boot sequences ,monitor those logs and use Ctrl-C when you see boot priority to interrupt boot sequence
2. Enter cli mode
8/0:boot>cli
8/0:cli>
3. Boot the image you saved.(see the above image name highlighted in red box)
boot Command Syntax
8/0:cli>boot -noconfig /flash/production.50091.asr5000.bin

## Slide 10
4.No Configuration found, press enter to continue. Press Enter
5. Do you wish to continue with the Quick Setup Wizard[yes/no]: no
(You can exit the Quick Setup Wizard by entering no in response to the above prompt.)
Press Enter button here

## Slide 11
6.Load the chassis with the latest configuration
--using command configure /flash/<file name>
After loading the configuration you will get # prompt.

## Slide 12
7.Then change the password of the user as shown

## Slide 13
Try to login with the new credential in other window.
WELCOME TO BANGALORE ASR5KLAB login:cisco
password:
Cisco System ASR5000
[local]asr5000#

## Slide 14
Thanks !!!