## Slide 1: Performing SMC/PSC/Demux card migration
Ruchi Shroti
Customer Support Engineer

## Slide 2: Table of Contents
Overview
Pre checks/Useful commands
Switch Management Card Migration
Packet Switch Card Migration
Demux Card Migration
Notes: So, when we talk of Service provider technologies, it was mostly SP MPLS, Frame-relay or ATM networks, i.e. mostly IP. i.e. SP Technologies basically enable the service providers to sell services based on IP.
Now, SP Mobility enables the service providers to provide mobility services to the end users.
The agenda will be something like this.

## Slide 3: Overview
In the event that an issue was discovered with an installed application or line card, depending on the severity, it may be necessary to take corrective action.
The system provides several redundancy and fail-over mechanisms to address issues with application and line cards in order to minimize system downtime and data loss. These mechanisms are described in the sections that follow.
This PPT will explain the migration of each of the card types(PSC/SMC/Demux ) available to the ASR5000. Appropriate administrator access is required for most procedures.
This PPT is divided in separate section for each type of card. Then each section is divided into separate sub-sections for each procedure .

## Slide 4: Pre Checks
show card table all
show rct stats (same is available in SSD as well)
Collect at least 2 SSDs(show support details) in interval of 15-10 mins.

## Slide 5: Useful commands
1.show card table all
it displays the chassis slot number and card type.
It will also display the operational state of the card. The possible operational states are:
Active: Indicates that the card is an active component that will be used to process subscriber data sessions.
Standby: Indicates that the card is a redundant component. Redundant components will become active through manual configuration or automatically should a failure occur.
Offline: Indicates that the card is installed but is not ready to process subscriber data sessions. This could be due to the fact that it is not completely installed (such as, the card interlock switch is not locked).

## Slide 6: Useful commands
2.Show rct stats :This command will give information about the switchover and migration happened in the chassis between different cards. Please find below example output
[local]# show rct stats
RCT stats Details (Last 3 Actions)
Action Type From To Start Time Duration
----------------- --------- ---- ---- ------------------------ ----------
Migration Planned 3 16 2015-Mar-27+09:59:47.248 0.850 sec
Migration Planned 4 3 2015-Apr-26+07:22:45.119 0.572 sec
Migration Planned 5 4 2015-May-08+11:10:13.559 0.886 sec
RCT stats Summary
-----------------
Migrations = 3, Average time = 0.770 sec
Switchovers = 0

## Slide 7: 1.SMC Migration
In the event that an issue arises that is not severe enough for the system to perform an automatic switchover, a manual switch over can be invoked please perform below steps
Verify the state of the SMC to be migrate.
******** show card table all *******
Tuesday April 28 11:08:13 IST 2015
Slot Card Type Oper State SPOF Attach
----------- -------------------------------------- ------------- ---- ------
...
8: SMC System Management Card Active No 24 25
9: SMC System Management Card Standby No - -
...

## Slide 8: SMC Migration continues..
2.Execute the following instructions from the Exec mode prompt:
Initiate a manual SMC switch over by entering the following command:
[local] #card switch from <active smc card number> to <standby smc card number>
You will receive the following prompt:
Are You Sure? [Yes|No]:
Press Y to start the switchover.
Note: You will lose your telnet or SSH session temporarily. Try to reconnect after a minute.

## Slide 9: SMC Migration continues..
3.Verify that the switchover was successful by entering the following command at the prompt: show card table .Check the entry in the Oper State column next to the SMC just switched. Its state should be Standby.
******** show card table all *******
Tuesday April 28 11:08:13 IST 2015
Slot Card Type Oper State SPOF Attach
----------- -------------------------------------- ------------- ---- ------
...
8: SMC System Management Card Standby No - -
9: SMC System Management Card Active No 24 25
...

## Slide 10: 2.PSC Migration
In the event of the critical failure of a packet processing card, tasks will be automatically be migrated from the active card to a redundant card in standby mode.
The line card installed behind the packet processing card that was formerly active will still be used to maintain the interfaces to external network equipment. Installed Redundancy Crossbar Cards (RCCs) will provide a path for signaling and data traffic between the line card and the now active packet processing card. Therefore, redundant packet processing cards do not require that line cards be installed behind them.

## Slide 11: PSC Migration Continues..
In the event that an issue arises that is not severe enough for the system to perform an automatic migration, a manual migration can be invoked. Follow the instructions below to manually initiate a packet processing card migration.
These instructions assume you are at the root prompt for the Exec mode:
Initiate a manual packet processing card migration by entering the following command:
card migrate from <original_slot#> to <final_slot#>
You will receive the following prompt:
Are You Sure? [Yes|No]:
Press Y to start the migration.
Please wait for some time and you will see that the state of both the cards got changed.

## Slide 12: PSC Migration Continues..
Verify that the migration was successful by entering the following command at the prompt:
show card table
Check the entry in the Oper State column next to the packet processing card that was just migrated from. Its state should be Standby. The state of the packet processing card migrated to should be Active.

## Slide 13: 3.Demux Card Migration
With session recovery (SR) enabled, this demux manager is usually established on one of the CPUs on the first active packet processing card.
Demux card contain many critical managers/processes.
Note : Demux card migration may result in service disruption, please contact TAC when you do this activity and do this activity during a Maintenance Window.

## Slide 14: Demux Card Migration continues..
You can find demux card by below command
[local]# show session recovery status verbose
Session Recovery Status:
Overall Status : Ready For Recovery
Last Status Update : 4 seconds ago
----sessmgr--- ----aaamgr---- demux
cpu state active standby active standby active status
---- ------- ------ ------- ------ ------- ------ -------------------------
3/0 Active 0 0 0 0 27 Good (Demux)
4/0 Active 24 1 24 1 0 Good
11/0 Active 24 1 24 1 0 Good
12/0 Active 24 1 24 1 0 Good
16/0 Standby 0 24 0 24 0 Good

## Slide 15: Demux Card Migration continues..
Please refer PSC Migration section as demux card is nothing but PSC.

## Slide 16
Thanks!!!