Lawrence Searcy

CSE, TAC Wireless

Lsearcy@cisco.com

## Introduction

This paper documents how to configure management access using a Microsoft IAS server. It does not cover the configuration part for the controller or configuring the controller as a radius client on the IAS.

## Background

The controller sends an access request with a service type of NAS Prompt (7) to the IAS radius server. For access, it expects to receive back not only an access accept but also a service type indicating the level of access.

## Configuration

- Create a new policy using custom policy

- Modify the policy conditions to authentication = PAP and Service-Type = NAS Prompt

NOTE: this assumes you have PAP configured on the controller under Controller->General->Web Radius Authentication. It may be changed to other methods.

NOTE: You should also have a Windows-Groups in the conditions for security reasons. The server will try to match the policy from 1 and continue down.

- Grant access

- Edit the profile

- Set the encryption of the incoming radius packet

- Select the advanced tab and set the service type to either:

  - Administrative  (Read/Write)

  - NAS Prompt (Read Only)

  - Callback Administrative (lobby ambassador)

## Troubleshooting:

- Errors will show up in the Event Viewer on Windows under Security.

- “debug aaa all enable” will show the outcome of the AAA request to the IAS

## Appendix A – Radius Packet Sent To the IAS for Management User Authentication

# Text boxes

Configuring Management Access on IAS