## Slide 1: Fast Track 2 - Small Business Switching – Module 3
Leah Davis
August 2011
Notes: Good morning everyone. Thanks very much for your time to join today’s Cisco Fast Track 2 Switching Module 3.

## Slide 2: Agenda
Switching 101: Switching Fundamentals
Which Switch? Choosing the Right Switch
Price Sensitive Customers: Unmanaged & Smart
Smaller Networks: Layer 2/2+ Managed
1
2
3
4
Larger Networks: Layer 3 & Borderless Networks
5
Competitive Positioning
6
Winning with Cisco: Programs & Promotions
7
Notes: In this module, we’ll cover what switching solutions to position with really price sensitive customers, and some of the pros and cons of those product choices.

## Slide 3: For Price Sensitive Customers
Unmanaged & Smart Switching
Notes: Many small business resellers are faced with customers who only look at two things on a project – price and payback. Often the business owner just wants to connect ports on desks, and for the IT purchaser, if there isn’t a regulatory requirement, it’s often a challenge to get money for equipment.
In a lot of cases, vendors may encourage you to throw in unmanaged switches onto the network to keep the quote down. Executives don’t want to hear about the differences between swtiches, but it’s very important to be aware of the pros and cons of your switch choices for price sensitive customers. There are huge implications in terms of security, scalability and reliability of the business in choosing a switch.

## Slide 4: Recommend “Built for Small Business”
Recommend Cisco Small Business products for customers who:
Are price conscious, but reliability is important
Want products that are easy to install and configure
Like browser-based management tool
Have smaller IP telephony deployments
Notes: This is particularly true for Small Businesses with less than 100 employees. The bottom line is that you cannot sell based on technology or feeds and speeds. What needs to be addressed is that price is not the only criteria. Small businesses tpically want products that are low maintenance, and that are reliable. Some small businesses will also want their network ‘futures-ready’ for technology like Voice over IP.

## Slide 5: A typical customer - unmanaged
Likely to be a smaller company
either self installed or a reseller is setting it up
Network is a tool and not core, likely to use email, web etc. but no or limited VoIP
This is usually more a reactive buyer – old switch broke, need a new one
Price sensitive
Not technical
Selling arguments: Cisco is #1, service and support, energy saving, Auto QoS - future proof, VoIP ready, TCO, ….
Notes: Unmanaged switches are primarily targeted for home and SOHO.
Typically the switch is self-installed, sometimes a reseller may set it up.
Unmanaged switches are typically positioned for networks that function as a tool for basic data connectivity to do things like email, web with no use of technologies like .
They will usually be purchased by more reactive buyers that are extremely price sensitive and not technical.
The customer will typically not be concerned about manageability, troubleshooting, uptime and security.

## Slide 6: Target Customers
SOHO
Small and Medium business
Healthcare
Government
Education K to 12
Campus networks
Manufacturing sites
The Smart switches product line is the answer for simple and basic networking scenarios where on top of the Data transmission, customers are looking forward to integrating Voice applications and are looking for resilience and redundancy
The Smart switch can be seen as a fundamentally managed switch designed for simple network configurations
Notes: Your target customers are small and medium business, and some of the verticals shown here. In some of these customer environments you will link unmanaged switches to connect ports on desks, and then link the unmanaged switches to managed devices.
As I said, most customers in this category are going to choose on budget and application. If you just want to set up a basic, network, a network unmanaged or smart-managed switches are good enough. If you need configuration options like like VLAN, QoS you will have to use a smart-managed switch (depending on the features they offer). One of the messages I’d really like you to take away today is that unmanaged switches are not appropriate for some types of deployments, and there are in my opinion many cons that can outweight the pros even for a price sensitive customer. In a LAN completely made up of unmanaged swtiches, a simple looping of a cable can bring the entire network to it’s knees.
For customers that need manageability and reliability, and particularly customers with high load networks or time critical applications with a lot of traffic, smart-managed is the minimum simply because most unmanaged switches don’t have the ability to identify and prioritize different traffic types like voice.

## Slide 7: Key Differences between Unmanaged and Managed Switches
Management interface
The ability to configure the switch and to prioritize LAN traffic
Unmanaged switch simply allows Ethernet devices to communicate with one another
  “Plug and play”
  Shipped with fixed configuration
Smart and Managed switches give you more control over your LAN
  Configure, manage, and monitor your LAN
  Advanced features to control traffic, and who has access to it
Notes: The key difference between unmanaged and smart or managed switches is that an unmanaged switch doesn’t have any kind of configuration interface or configuration options. They are plug-and-play, so you only need to connect your computer or other network devices to the unmanaged switch directly. If there are no advanced applications needed, the unmanaged switch can be an okay choice. Normally, the unmanaged switch will be found in the home, SOHO or small business.
An unmanaged switch simply allows Ethernet devices to communicate with one another, such as a PC or network printer. The benefit of an unmanaged switch over a hub are full bandwidth to each port, rather than broadcasting all data over all the ports like a hubs and dealing with collisions.
Unmanaged switches allows all traffic to go all through your network and while this is happening you have no control over the data which is coming inside the network or going outside. While if you have a managed switch you can simply have very good control over the data and it will allows ports to talk to further ports or discard at all.
Smart-Managed switches are recommended for small to medium sized business users who may need some or certain configurations and control over the network. Smart Managed switches are somewhere in between unmanaged and managed Layer 2 switches. They have more features as unmanaged switches but only allow a certain amount of individual configuration via web interface. So you can do basic management and configure features to ensure network security and reliability, but all the bells and whistles of an advanced switch aren’t there.
Many other vendors offer smart switches with no CLI (command line configuration), but Cisco Small Business Smart Switches offer a full CLI.

## Slide 8: Cisco SB Switch Maintenance Release
Available now – free (no service contract required)
Firmware enhancements to Cisco Small Business200 & 300 series:
Command line reference guide: http://www.cisco.com/en/US/products/ps10898/prod_command_reference_list.html
Feature | Benefit | 200 | 300
CDP | Auto-discovery of connected Cisco devices | X | X
Smartports | Auto-configuration of port based on CDP info | X | X
XML API | CCA Management application support | X | X
TextView | Command Line Interface |  | X
Secure Copy | Secure way to upload/download config files |  | X*
Web Authentication | When enable, user must authenticate before given full access |  | X*
Disable Inter-VLAN routing | Simplifies deployment of routing |  | X
Q-in-Q VLAN Tagging | Double VLAN tagging – mainly used in Metro Area Networks (MANs) |  | X
* Items available in releases after 1.1
Notes: A maintenance release for the 300 Series and 200 Series switches is now downloadable from Cisco.com, and it’s free – there is no service contract required – just download it. Not all stock is going to have this firmware release, so please ensure that you upgrade any existing install switch as well as new ordered stock to this firmware as soon as possible. There is about 7-12 weeks between when stock on shelf will have this new firmware release.
This maintenance release will bring in:
A voice feature set on the switches. What that does is implement the ability to detect a Cisco UC device like UC500 or UC300 advertising a voice vlan with Cisco Discovery Protocol (CDP), automatically create that voice van, set up ports dynamically as ip phone plus desktop, and implement autoports or smartport functionality, so you can plug in an access point to one of those phones, etc. That voice feature set will be available on both the 200 and 300 series switches.
We have introduced a full command line interface or CLI called Textview for text-based configuration or for mass deployments.
There will also be management hooks for cca to be able to manage these switches with an XML API, and there is a plan for a future CCA release to discover these switches, but that CCA release will be before the end of the CY.
When you go to cisco.com software download center, choose Cisco Samll Business 200 or 300 series Managed Switches and there is one image that serves the complete series of switches, no matter the port density.
There is a command line CLI reference guide available now at the link at bottom of this slide. This explains in detail all the individual features.

## Slide 9: Unmanaged Switches
Internet
Basic Connectivity
Basic Management
Advanced Management Options
Basic QoS
Advanced QoS
VLAN
VoIP Ready
Video
CLI
Stacking










Notes: Choose the Cisco Unmanaged Switch if you need:
A simple network
Basic connectivity*
End-user installation and support
Smaller (non-rack-mountable) form factor
*No management, no VLANs, not ready for voice or video
Unmanageable switch comes with default setting and L2 switching functionality. There is no management on an unmanaged switch.
As I said, there are quite a few risks of using an unmanaged switch. If something goes wrong, you may have to go around to every switch in the place and reboot it to get it back on the network and you may still end up having packet loss on the network. If by mistake you take an unmanaged switch and uplink it twice to the network, or to another switch two times, you can also get a network loop, which can bring the whole network to a standstill. This is because unmanaged switches also lack protocols such as Spanning Tree Protocol, which prevent loops in the network. Smart and managed switches prevent all of this by STP and portfast.

## Slide 10: Cisco 100 Series Product Overview
Unmanaged Layer-2 switches, 5 to 24 port, FE and GE models
Zero configuration; Zero customization
Energy-Efficient Technology (Gigabit models)
QoS for better voice, video and multimedia performance
Fan-less design for quiet operation
Desktop and rack-mount
Supported by small business support center with CCNA-certified staff
Limited Lifetime warranty
Notes: Cisco 100 Series switches are a line of unmanaged switches that provide wire-speed Fast Ethernet and Gigabit Ethernet connectivity in either desktop or rack mount models.
These switches work out of the box and require no configuration – they’re really designed to be plug an dplay. They feature a fanless design for quiet operation and provide unmanaged connectivity.
The 100 series offers some features such as quality of service (QoS) and green efficient technology that saves power and reduces costs. I’ll talk to QoS on the next slide.
These switches offer peace of mind with a limited lifetime warranty and are supported by the Cisco Small Business Support Center.

## Slide 11: Quality of Service in 100 Series
Integrated Quality of Service (QoS)
Zero configuration is required by the user
Switch is able to read 802.1p tags and prioritize traffic accordingly
Automatically prioritizes traffic based on priority mapping
Uses standard 802.1p class of service (CoS) settings
Set with the same default QoS settings as the Cisco SPA IP phones and IP cameras
  Simply connect Cisco IP phones and cameras to 100 Series switches
  No configuration required based on default QoS settings
Layer 3 QoS (differentiated services code point [DSCP]) is not affected
  - 100 Series are Layer 2 switches and do not read L3 QoS tags
Notes: Quality of service allows you to prioritize your network traffic by assigning a higher priority to critical traffic. This helps ensure consistent network performance and can support delay-sensitive data such as real-time voice. For instance, if I know I have voice packets traveling over my network, I want to make sure they have the highest priority so that these voice packets don’t get dropped or delayed and mangle a phone conversation.
While there is no management interface on Cisco’s unmanaged switches, there is a level of quality of service on the 100 series switches to help applications run smoothly. There is basic traffic prioritization on the switches – all received packets are examined for QoS priority encoding. The switch reads the 802.p class of service or priority level and forwards the packet based on that priority level. For example, during heavy loads voice and video traffic are given priority over data traffic. So if you plug in a phone, the switch will automatically comply with 802.1p tagged frames. This ensures that time-sensitive traffic like voice gets the highest level of service.
To prioritize voice or video traffic by using the QoS feature on the unmanaged switch, you set flow control to off in the configurations of
the connected devices like phones.

## Slide 12: Cisco 100 Series Switch Model Overview
SF 102-24
24 10/100 Ports
2 Combo mini-GBIC ports
SF 100-24
24 10/100/100 Ports
SF 100D-16
16 10/100/ Ports
SF 100D-16
16 10/100/ Ports
SF 100D-08
8 10/100 Ports
SF 100D-05
5 10/100 Ports
SG 100-16
16 10/100/1000 Ports
SG 102-24
Compact size
22 10/100/1000 Ports
2 Combo mini-GBIC Ports
SG 100-24
22 10/100/1000 Ports
2 Combo mini-GBIC ports
SG 100D-08
8 10/100/1000 Ports
Fast Ethernet
Gigabit Ethernet
Notes: 12
Here are the Cisco 100 Series unmanaged switch models – there are Fast and Gigabit Ethernet, PoE and non-PoE and desktop and rackmount models – all have a limited lifetime hardware warranty with return-to-factory replacement and a 1-year warranty for fans and power supplies. They are positioned as switches with no installation software and nothing to configure, providing an affordable reliable switch infrastructure.

## Slide 13: Important Portfolio Enhancements
Improvement | Customer Benefit
Energy-Efficient Technology | Reduced power consumption and energy costs
Fanless Designs | Quiet operation and increased mean time between failures (MTBF)
Additional usable Gigabit Ethernet ports on Gigabit Ethernet models | Ability to connect more devices and better value for the purchase
IPv6 | Ability to evolve network and support next-generation OS
Localized GUIs and Documents | Clarity of product installation in select markets
Simplified configuration with additional management options, FindIT toolbar | Ease of installation and multiple management options for optimal deployment and support
Lifetime Warranty | Investment protection
Notes: Here are some of the portfolio benefits of the 100 series unmanaged switches mapped to customer benefit.
These unmanaged switches are designed to optimize power usage, they’re largely fanless to reduce noise in a small business environment, and the switch supports IPv6 addressing. There is also the lifetime warranty – the limited part means that it applies to the original owner and if Cisco EoS/EoL the switch, the warranty continues for 5 years after the EoS/EoL date.

## Slide 14: Why pay more for a Smart Switch?
When you need more input and control over the customer network
  You get many additional features with a Smart switch
  Quality of service, virtual LANs, redundancy, and port mirroring
  VLANs – logically group devices
When you need Redundancy
  Safeguard a network in case a connection or cable fails with alternate data path for traffic
  Spanning Tree Protocol (STP) provides path redundancy in the network
When you need tools to Troubleshoot the network
  Port Mirroring – helpful to diagnose problems
Notes: Why pay more for a Smart switch? Each business needs to evaluate the needs of their network. If your customer’s network requirements are at the point where they would like to have some input and control over the behavior of traffic on their LAN, or if you need some level of redundancy or troubleshooting capability, then it is a good time to consider a smart switch, which is a manageable switch.
Also, if you are planning to deploy advanced services such as wireless LANs or IP telephony in the near future, smart and managed switches can lay the foundation for these technologies.
The ability to control and segment network traffic helps reduce unnecessary traffic. For instance, you can segment traffic between your finance and marketing groups, so that mission-critical finance information can flow without delay to the finance users and not get bogged down by marketing traffic. This allows better network performance and in many cases provides an additional level of security.
Another important feature of a managed switch is redundancy. Redundancy provides the ability to safeguard a network in case a connection or cable fails by providing an alternate data path for traffic. Managed switches incorporate what is called Spanning Tree Protocol standard, or STP, to provide path redundancy in the network. Using the spanning-tree algorithm, STP provides redundant paths while preventing loops that are created by multiple active paths between switches. STP allows for one active path at a time between two network devices, preventing loops and establishing the redundant links as a backup to keep integrated systems available and preventing
expensive downtime.
And, finally, there are troubleshooting capabilities like port mirroring. In conjunction with a network analyzer, this feature is useful to diagnose problems. It copies the switch network traffic and forwards it to a single port on the same switch for analysis by a network analyzer. You can use the analyzer on a monitor port to troubleshoot network problems by examining traffic on other ports or segments. The benefit of this is you can troubleshoot problems without taking the network out of service.

## Slide 15: A typical customer - Smart
Very small company but technical aware, price sensitive customer at the network edge (can even be quite big installations)
Self installed by “the technical guy” or by the reseller / VAR
Understand the need for VLAN, QoS.
Either VoIP today or interested for the future
Network is important, but not core. Usually have an IT budget and have a buying plan vers. being reactive
Price sensitive – but do understand that functions do have a price
Technology aware
Selling arguments: Cisco is #1, service and support, energy saving, management option, VoIP and other real time traffic, …
Notes: The typical customer for a Smart switch is a price sensitive small business customer that is aware of the need for a network that they can control and manage. They are technology aware and may be either interested in VoIP today or in the future. The network is important but not a core part of the business. The target customer will usually have an IT budget and a buying plan vs. being reactive. They’ll also understand that functions do have a price. They’ll want to build a basic network with performance ad reliability, with easy-to-use management at a great price.

## Slide 16: Smart Switches
Internet
Basic Connectivity
Basic Management
Advanced Management Options
Basic QoS
Advanced QoS
VLAN
VoIP
Video
CLI
Stacking










SLM2008-K9
SLM2008-K9
SLM2024-K9
WAP200
Upsell: Add Business Class Wireless, add VoIP, Video Sur. Alternative: Position Smart switches as edge switches
Notes: What makes a smart switch ‘smart’? For the typical non-techhy user, the web smart switch is friendly. You don’t need to remember commands, and you can use the web interface to configure the switch. You won’t be able to manage the smart switch via SNMP,CLI ,telnet.
Smart switches supports basic settings, such as VLAN segmentation, MAC address binding, rate limit setting and so on.
There are basic QoS capabilities including basic queuing, mapping CoS/802.1p and DSCP (differentiated services code point) values to egress queues and configuring bandwidth.
Security features include the ability to define users, configure RADIUS parameters and management access authentication, define access profiles, configure TCP/UP services and storm control, and also to configure port security and identity based networking capabilities such as 802.1x.
The price of web smart switch is much lower than full managed switch, so if you only want to build a simple business network with important features like quality of service and basic network security, these Smart switches are a great choice.

## Slide 17: Cisco 200 Series Switches Purchase Decision
Basic managed features at an affordable price
Basic network features
  Security
  QoS
  IPv6
Easy-to-install products with web-based management tools
Ability to manage network traffic
Value led
Small Business Support Center
Notes: The Cisco 200 series smart switches can be easily positioned to the price sensitive customer as a switch that will deliver basic managed features at an affordable price. They get numerous features to achieve a business-class network with those important capabilities like QoS, PoE and IPv6. They’re very easy to install and setup with a browser-based configuration interface. The performance is very good, so you can feel comfortable selling this product to a value customer. Support is from Cisco’s Small Business Support Center, which runs 24x7 globally.

## Slide 18: Energy-Efficient Technology Auto Power-Down
Automatically turns off power on Gigabit Ethernet RJ-45 port when detecting link down
  If there is no link on a port (when there is no connection or the device connected is turned off), the port(s) enter a “sleep mode”
Resumes active mode when the switch detects the link up or device connected
  The switch sends out electrical pulses at frequent intervals
Adjusts power based on cable length (on Gigabit Ethernet models)
Detects the length of connected Ethernet cable and adjusts power usage accordingly—without affecting performance
Notes: The switches have an energy efficient design that conserves energy by optimizing power use and lowers energy costs; ports power down automatically when a link is down. The switch also adjusts power usage based on cable length.
802.3 Energy Efficient Ethernet (EEE) is used to achieve these power efficiencies, though note that the attached device must support EEE also.

## Slide 19: Cisco 200 Series Product Overview
Next-generation Cisco smart switches
24 and 48-port models Fast Ethernet and 8 to 50-port models Gigabit Ethernet, Power over Ethernet (PoE)
Enhanced features, including QoS, IPv6, and remote management
Improved power efficiency with low-power hardware and fanless designs
Localized into 7 languages, both GUI and documentation
Supported by the Small Business Support Center with Cisco CCNA® certified staff
Limited lifetime warranty
New!
Notes: These 200 series switches replace the old SLM switches (there is a legacy reference to SLM in the product name but they’re entirely new hardware and software). These smart switches will help you achieve a basic business-class network with important features like QoS, PoE and Ipv6 support on a switch that’s very easy to use with a limited lifetime warranty.

## Slide 20: Cisco 200 Series Switches Model Overview
SF200-24
24 10/100 Ports
2 Combo Mini-GBIC Ports
SF200-24P
24 10/100 PoE Ports
2 Combo Mini-GBIC Ports
Fast Ethernet
SF200-48
48 10/100 Ports
2 Combo Mini-GBIC Ports
SF200-48P
48 10/100 PoE Ports
2 Combo Mini-GBIC Ports
SG200-18
16 10/100/1000 Ports
2 Combo Mini-GBIC Ports
SG200-26
24 10/100/1000 Ports
2 Combo Mini-GBIC Ports
Gigabit Ethernet
SG200-26P
24 10/100/1000 PoE Ports
2 Combo Mini-GBIC Ports
SG200-50
48 10/100/1000 Ports
2 Combo Mini-GBIC Ports
SG200-50P
48 10/100/1000 PoE Ports
2 Combo Mini-GBIC Ports
New!
Notes: 20
Choose from 24 and 48 ports of Fast Ethernet or 8 to 50 ports of Gigabit Ethernet connectivity
Power over Ethernet (PoE) is available on up to 48 ports of Fast Ethernet and 50 ports of Gigabit Ethernet

## Slide 21: Cisco 200 Series Switches Comparison
 | Cisco SLM Switches | Cisco 200 Series Switches
Product Name Change | – | Yes
Energy-Efficient Technology | No | Yes
Additional Gigabit Ethernet Ports | Standard | Two additional on Gigabit Ethernet models
IPv6 | – | All models
Management and Configuration | GUI and menu command-line interface (CLI) | GUI, Cisco Discovery Protocol, Smartports, and Small Business FindIT
Localization and Globalization | English only | Seven languages: GUI, documents, and support
Warranty | Five years | Limited lifetime
Notes: New to the portfolio is the addition of energy efficient technology. As I mentioned, these switches optimize power use to protect the environment and reduce energy costs, without compromising performance.
A fanless design has been added to more model so that they run silently and unobtrusively.
A key enhancement is the addition of more ports across the Gigabit Ethernet portfolio.
The Cisco 200 Series provides native support for IPv6, the newest version of the Internet Protocol, as well as the previous IPv4 standard. You will be able to move up to the next generation of networking applications and operating systems without an extensive equipment upgrade.
The base feature capabilities remain the same as the old SLM feature sets. So for example all SKus provide full line rate with a non-blocking architecture and support for support for IEEE 802.1D spanning tree and IEEE 802.1Q with full line rate forwarding. Other features on the 200 series include:
  Support for next-generation ip addressing with IPv6
  Support for IEEE 802.3af-powered devices, which means you don’t need to run additional power outlets for devices like IP phones, wireless access points, and surveillance cameras.
  support for per port configuration, status, utilization, and monitoring.
  more capabilities for diagnostic analysis and troubleshooting, including hardware port mirroring.
  Support for a minimum of 8000 MAC addresses
  Support for shared as well as independent VLAN learning
  the ability to configure Port VLAND IDs and port VLAN priority as well as ingress filtering.
  Support for Multiple Spanning tree and Rapid Spanning tree (or PVST in Cisco Classic terms) fast convergence, link aggregation (802.1ad),
  Support for QoS and rate limiting by port, link aggregation group, vlan or access control list.
  Supprot for IPv6.
  Support for CLI and smarports

## Slide 22: 200 Series Competition
 | Cisco | Netgear | D-Link | HP
Value Prop from the Competitor | Best feature/price offer Solution Integration Superior solutions & service | Price Green | Price Green Industry Solutions | Strong business brand Warranty
Sell Against | Cisco 200 Series Switches | FS7x, GS7x | DES12xx, 325x, DGS12xx | 1700, 1800, V1905, V1910
Strengths | Comprehensive portfolio Complete networking product, solutions, and services offerings SB Investment Protection Program | Price Transactional point products | Price Transactional point products | Lifetime warranty with NBD Brand Small Office product attach i.e. printers, servers etc
Weakness | No NBD on warranty | Limited networking product, solutions and services portfolio Support is not strong | Limited networking product, solutions and services portfolio Support is not strong | Limited switch portfolio Limited networking product & solutions portfolio Command price premium Support is not strong
Notes: Cisco positions these Cisco 200 series as offering the best value/feature mix and is priced lower than key competitors. There are a lot of smarts in saving power, enhanced features for IPv6 across all models, QoS and security, additional ports on Gigabit Ethernet models, plus Cisco quality and reliability. Very important, 200 series switches are easy to manage and includes a limited lifetime warranty.
Comparisons to other vendors are shown here – most other vendors have a much more limited switch portfolio at higher prices than what Cisco offers with these Small Business switches.
As a partner, these 200 series switches are going to enable you to sell a price sensitive customer a switch with high-speed network connectivity and many of the same Quality-of-Service and Security features found in more expensive full Layer 2 managed switches but without their complexity – backed by the Cisco brand and Cisco support.

## Slide 23: Resources and URLs
Cisco 100 Series Switches http://www.cisco.com/cisco/web/solutions/small_business/products/routers_switches/100_series_switches/index.html-tab-ForPartners
Cisco 200 Series Switches http://www.cisco.com/cisco/web/solutions/small_business/products/routers_switches/200_series_switches/index.html-tab-ForPartners
Partner Central Small Business Switching www.cisco.com/go/smbpartner/switching
Cisco Small Business Support Community https://www.myciscocommunity.com/community/smallbizsupport
Cisco 100 Series Switches Warranty http://www.Cisco.com/go/warranty
Cisco Small Business Service www.cisco.com/go/smbservices
Notes: Here are some resources.

## Slide 24: Quick Quiz

## Slide 25: Quiz Rules
One question based on presentation content
First correct answer in the chat window wins a $100 pre-paid VISA card
Make sure your chat is directed to Everyone or Panelists
Get Ready…

## Slide 26: Which is NOT a key difference between a smart and unmanaged switch? A: Fixed configuration C: More control over the LAN D: Management interface E: Price
Notes: Correct answer: A - both smart and unmanaged switches can be fixed configuration devices.
A reminder to please complete the poll at the end of this session. Thank you very much for your time and have a great day!

## Slide 28: Switch PoE Summary
Only 802.3af PoE for SBTG switches
802.3at is planned for 5xx series
No Cisco inline power (only some „older“ Cisco products do support the Cisco inline power only – e.g. Some older phones)
Smart with PoE: ½ the ports at 7.5 Watt , ¼ of the ports at 15.4 Watt
SRW, SFE &SGE with PoE All ports at 7.5 Watt, ½ the ports at 15.4 Watts
Exception: SRW2xx8MP-K9 All ports at 15.4 Watt
Any possbible combination as long as the overall PoE budget is not exceeded