## Slide 1: Switching 101
Switching Fundamentals

## Slide 2: Layer 2 vs. Layer 3 Switching
Hubs broadcast all received traffic (not efficient)
Layer 2 switches provide more efficient network traffic patterns than hubs
  Separate VLANs (subnets) can be typically be created
  Layer 2+ switches perform static routing functions between VLANs
Layer 3 switches perform dynamic routing functions and can make use of the IP information inside the packet
  Dynamic routing between separate subnets
  Typically more expensive than Layer 2/2+ switches
Notes: You’ll also need to determine whether you need layer 2 or layer 3 switches. In the ISO/OSI model, layer 2 is the Data Link layer where the source and destination terminals are identified by MAC addresses in the network packet. A layer 2 switch can use this information to build a switching table to identify which port a particular MAC address/machine is on. This results in much more efficient network traffic patterns than with hubs, which simply broadcast all received traffic.
Conversely, in the ISO/OSI model, layer 3 is the Network layer where IP and routers also operate. As such, a layer 3 switch can perform routing functions since it can make use of the IP information inside the packet.
In general, smart switches are Layer 2 devices, just like unmanaged switches. Both operate at the Data Link layer, which handles physical addressing. Simply put, Layer 2 devices can look only at the MAC address and LLC portions of a data packet's Ethernet frame.
On the other hand, you can find managed switches in both Layer 2 and Layer 3 flavors. Layer 3 switches operate at the Network Layer, which provides network path determination and logical addressing functions. In most cases, this means that Layer 3 switches handle packets based on their IP address, which allows them to perform basic routing functions.
For smaller networks that are centrally located and located in a single subnet, a layer 2 switch is more than sufficient. As networks begin to grow and users are broken out onto separate subnets in order to improve network efficiency and provide better traffic flow, layer 3 switching/routing becomes the better choice.

## Slide 3: Smart and Managed Switch Differences Smart Switches Are Not the Same as Managed Switches
  Basic Features
VLAN
Link aggregation
Port mirroring
Internet Group Management Protocol (IGMP)
Spanning Tree Protocol (STP)
  Basic QoS
  Trust endpoints (computer, phones, access points, etc.) to set prioritization
  Basic Security
  Endpoint authentication: 802.1x
  Basic Web Management
  Web management
SMART Basic
Intelligence in Switch/Network
Allow/disallow/prioritize users, applications, and workgroups
Control performance of application
Scale/Grow Network
Larger number of VLANs
Flexibility for Application Deployment
MAC-based , guest, and private VLANs
Security
Highly secure management (Simple Network Management Protocol [SNMP] v3, SSH/SSL)
Management Visibility
Management: SNMP, CLI, web GUI, cloud
MANAGED Advanced
Notes: Prices of managed and smart switches have come down dramatically, as feature sets and ease of use have expanded and improved. With eight-port Gigabit "smart" switches now available for under $100, smart and managed switches are a good choice for small business. We’ll start with a brief overview on what makes a smart switch "smart".
Basically, smart / managed switches have features that can be configured to perform network management functions. These functions can be as simple as setting the link speed of a port or disabling it entirely, or more complex like limiting bandwidth or grouping devices into VLANs.
At this point, the difference between "smart" and a "managed" switches is strictly marketing. The term "smart" switch was coined when network product manufacturers first introduced lower-priced managed switches.
It is important to note that these days a Smart Switch is not the same as managed switch. While it may be easy to believe a smart switch is the same as a managed, there are some clear differences.
Smart switches trust that the endpoints, such as computers, phones and access points to set the right level of network traffic prioritization. If the endpoint classifies it incorrectly, network performance will not be optimized. In the case of a managed switch, you set the priority level to ensure optimal network performance,
Next smart switches include basic port security. Managed switches provide more extensive features that protect network traffic including access control lists (ACLs) to restrict sensitive portions of the network from unauthorized users and guard against network attacks, virtual LANs (VLANs) to let you provide segment network traffic and support for secure management control using protocols such as SNMPv3 and SSH/SSL.
Lastly smart switches have basic management capabilities. Whereas with a managed switch you control all aspects of the network traffic.

## Slide 4: Scaling up: VLAN Separation by Functional Group
VLAN 4
Marketing
VLAN 3
Engineering
VLAN 5
Management
Best Practice: A “Management VLAN” is for IT Staff only to configure the network. A separate VLAN provides additional security for your network. Users will not be able to access the configuration for network devices
VLAN 2
Voice
Notes: VLANs may be assigned based on a number of different attributes, such as by application type including voice or data. It is also logical to subdivide the network based on functional groups, such as Sales, Engineering, Marketing and Network Management. Such groupings typically bring resources into closer proximity to the users which improves network performance and may simplify QoS implementation requirements for applications such as CRM or ERP type systems. CRM and ERP systems have business-critical requirements that are beyond a normal IP “best-effort” performance capability. Security for sensitive resources such as the HR database or the payroll system may also be protected from unauthorized access by placing these servers on a separate VLAN. Some examples of VLAN implementations include creating VLANs for applications like IP phones and functional groups such as Engineering or Human Resources. Next, we’ll take a more detailed look at security from a networking perspective.

## Slide 5: Scaling up: Dynamic VLAN assignment - GVRP
C
A
IP Voice
VLAN
A
IP Data
VLAN
B
C
B
GVRP - Generic Attribute Reservation Protocol (GARP) VLAN Registration Protocol
Adds VLANs automatically to the backbone (switches), if device requests that VLAN
Switch 1 configured with all VLANs
After D is connected, switch 2 requests “Voice” VLAN trunk with switch 1 using GVRP
D
2
1
GVRP
Voice
VLAN
Notes: When VLANs are used to segregate traffic, it improves the security capability of the network since business critical resources can be placed onto separate internal subnets. Access may be controlled and granted through routers. Using VLANs can simplify the implementation of Quality of Service capabilities because QoS sensitive devices may be placed on a specific VLAN ID. This simplifies the recognition task for the switches, routers or server adapters that need to prioritize traffic. VLANs can also improve the reliability and scalability of the network by distributing the normal IP networking workload across separate networks and multiple devices. Implementing VLANs requires the ability to manage the switch so unmanaged switch or hub devices cannot be configured with VLANs. One of the functions that can be automated is the assignment of VLANs across the network. GVRP (Generic Attribute Reservation Protocol {GARP} VLAN Registration Protocol) allows the switch infrastructure to automatically assign VLANs across the backbone as devices attach to the edge of the network and request connectivity to the infrastructure. This allows mobile devices, which have been pre-assigned to a specific VLAN, to gain access from potentially any location on the backbone. One master switch is assigned all of the VLANs that are configured on the network. Once a device connects to the edge of the network, it attempts to forward packets using a specific 802.1Q VLAN ID. The switches use GVRP to connect with the master switch and request that a trunk.

## Slide 6: Feature: Link Aggregation
Combines two or more physical ports to one logical port
Enhanced Performance
Use: Switch to Switch Link
Connect Server to the network
Also works with GB Ethernet Ports

## Slide 7: The Problem: Multiple Connections
Two or more redundant connections somewhere in the network result in:
  Packets are doubled
  Performance Loss
  Extended Overhead
  Manual Search for Error

## Slide 8: The Solution 1: Spanning Tree (IEEE 802.1d)
Switches will Auto-Negotiate the Preferred Route and create a logical tree structure
If Preferred Route is faulty, Non-Preferred Route will act as the backup
Advantage: Automatic setup and negotiation
Disadvantage: If a preferred route is faulty, it can take up to 30 seconds to re-organize the logical tree

## Slide 9: The Solution II: Rapid Spanning Tree (IEEE 802.1w)
Rapid Spanning Tree
If a preferred route is faulty, the network will continue to work
The new logical tree will be automatically calculated
If the new tree is ready, it will be setup within 1 second

## Slide 10: The Solution III: Multiple Spanning Tree
Inspired from Cisco’s MISTP implementation
Abstract: Used to efficiently implement “Spanning Tree” for VLAN’s
Base Idea: Several VLAN’s can be mapped to a reduced number of spanning Tree instances
Increases Network Performance
Decreases CPU utilization

## Slide 11: What are the Performance/QoS services?
Capability
Benefit
Management
Scalability
Reliability
Security
Performance
Classification
  Recognizing packets and determining QoS required
    Access Control Lists for packet classification
Marking
  Setting the QoS parameters in the packet
  DiffServ Code Point (DSCP) – layer 3
  802.1p – layer 2
Queuing
  Implementing the QoS required
  Putting packets into a priority queue
Shaping
  Policing (rate control of input)
  Shaping (rate control of output)
Applications with real-time requirements are sensitive to latency and jitter
  Voice
  Video Tele-Conferencing
  Require highest priority service
Applications without real-time requirements (buffering in the media player) that are also sensitive to jitter
  Video distribution
  Video surveillance
  Require next highest priority of service
Protecting the network from rogue users consuming more than their fair share of resources
  Ensure non-priority application/users are in low priority service class
Delay
Delay Variation (Jitter)
Loss
Notes: 28
Now we’ll look at ensuring a proper level of performance for the applications that are providing mission critical services on the IP network such as voice. As was discussed in the TDM Voice section at the start of this class, voice communication typically has a real-time requirement that makes it very sensitive to latency and jitter. Latency is the time it takes for information to get from the source to the destination and jitter is the variation from the expected arrival time at the destination for each individual packet of voice information. Too much latency and/or jitter in the voice stream will affect the actual usability of the voice service. As we’ve seen from the procedure that IP network devices use to forward packets, this means that we need to prioritize the voice traffic so that it gets processed first, providing the minimum latency and jitter. Video shares many of the same characteristics with voice, but doesn’t generally (except for Video Teleconferencing) require real-time service. Video applications can generally deal with latency since the media players that are typically used for playback include buffering in their viewing process. However, jitter still has a negative effect on video performance so video applications do require the next highest prioritization in an IP network. We would also like to keep any rogue users out of the high priority service classes to protect our voice and video traffic. By assigning rogue users to the “Best Effort” priority queue, they should receive an adequate level of service. With an infrastructure that supports rate control, we can limit the amount of bandwidth that rogue users have access to, further limiting the effect they can have on other users and applications.

## Slide 12: Bandwidth Control
Rate Control
  Switch controls the rate of traffic coming into (Ingress Rate) or out of (Egress Rate) a physical port
  Layer 2 switches can’t rate limit specific services (e.g. FTP) or by IP address
Priority Based QoS
  Handle packet priority via DSCP (Diffserv) or 802.1p
  Both are protocols for communicating the priority of network packets
  802.1p is a Layer 2 protocol (L2/L2+ switches) – LAN only
  DSCP is Layer 3 protocol (L3 switches)
Notes: With rate control, you can control the rate of traffic coming into (Ingress Rate) or out of (Egress Rate) a port,
Note that because a L2/L2+ switch are a Layer 2 device, they can't rate limit specific services such as BitTorrent, FTP, etc. and it also can't rate limit by IP address. Rate limiting works only by physical port and all traffic through that port.
Priority based QoS means the switch canhandle packet priority via DSCP (Diffserv) or 802.1p. Both are protocols for communicating the priority of network packets, with the difference being that 802.1p is a Layer 2 protocol and DSCP is Layer 3.
The significance of the difference is that choosing 802.1p means that traffic will be prioritized on your LAN only. As a Layer 3 protocol, DSCP will survive going through routers (assuming they are DSCP-capable) and generally is considered more robust. DSCP also has the advantage of being visible to network sniffers like Wireshark, where 802.1p tags generally aren't.

## Slide 13: Switch Forwarding Modes
Store-and-forward mode:
  Supports error checking and packet filtering
  Forwarding mode of choice as it also supports the conversion of LAN speeds, which is a bridging function
Cut-through mode:
  Skips error checking
  Doesn’t support either packet filtering or switching between different LAN speeds
Fragment-free mode:
  Cut-through forwarding
  Limited error correction capability - packets below the minimum allowable size (runts) discarded
Notes: Most switches offer up to three possible ways for packets to be forwarded through the unit:
Store-and-forward mode: This method supports error checking and packet filtering since the entire packet is read into the switch’s memory and read before being forwarded to the appropriate switch port. Because the switch needs to receive the entire packet, this forwarding mode results in the highest transit delay. For 10/100 switches with a mixture of 10-Mbps and 100-Mbps devices, this is the forwarding mode of choice as it also supports the conversion of LAN speeds, which is a bridging function.
Cut-through mode: Unlike store-and-forward, this forwarding method skips error checking, and it doesn’t support either packet filtering or switching between different LAN speeds. Enough of the incoming packets are read to determine their destination, and the entire packet is then immediately forwarded to the destination MAC address. Because of the speed at which this mode operates, error packets are forwarded along with good packets.
Fragment-free mode: This is cut-through forwarding with limited error correction capability since packets below the minimum allowable size (runts) are discarded.
The mode you look for in a new switch depends on the devices that you’ll be supporting. If you have both 10-Mbps and 100-Mbps devices, you’ll need the support of store-and-forward’s bridging features. If, however, your devices all run at 100 Mbps, you can enjoy the lower latency of cut-through forwarding or fragment-free forwarding for a reduced number of potential errors.

## Slide 14: Switch Speeds
Switching speed
  Speed at which a switch can process traffic coming in and send it back out
Backplane speed/switch fabric speed
  How fast traffic can be transmitted between modules in a switch
Blocking and nonblocking
  Define whether or not a switch can support all ports transmitting simultaneously at their highest possible speeds
  Nonblocking is better choice for large amounts of traffic
Buffer size
  Fixed amount of storage is dedicated to each port, or every port shares a common buffer storage area
  Can impact speed at which a switch can forward packets
Notes: Switching speed
Switching speed is the speed at which a switch can process traffic coming in and send it back out. This is not the same as the bandwidth or backplane speed. Switching speed is generally measured in millions of packets per second—the higher the switching speed, the better.
Backplane speed/switch fabric speed
The backplane speed measures how fast traffic can be transmitted between modules in a switch. Closely related to blocking and nonblocking, this number needs to be sufficient to handle your most extreme loads across the switch.
Blocking and nonblocking
Blocking and nonblocking define whether or not a switch’s internal communication and packet processing power can support all ports transmitting simultaneously at their highest possible speeds. A nonblocking switch has enough horsepower to handle this condition, but a blocking switch may need to throttle back traffic in order to handle it all, resulting in a potential bottleneck.
Which architecture is best for your needs depends on what your users primarily do on the network. If they are constantly transferring large files across the network, a nonblocking architecture is a better choice. If, on the other hand, your users spend their days dealing with e-mail and doing Web research, a lower-speed backplane will more than suit your needs.
Buffer size
Every switch has some sort of buffering mechanism. In most cases, either a fixed amount of storage is dedicated to each port, or every port shares a common buffer storage area. The buffer size can have a direct impact on the speed at which a switch can forward packets. A buffer that is too small will cause a switch to throttle back traffic in an effort to control network congestion.

## Slide 15: Switch Security
Port Security
  Access Control Lists (ACLs) define traffic patterns (filter and actions) for ingress traffic
  Traffic from any other device physically connected to the port or LAG with active ACL be discarded, forwarded, given a specific QoS, etc
Port Authentication
  Users login or authenticate to access LAN (e.g. with RADIUS server)
  Different access profiles, rules and filters can be used to authenticate and authorized users
TCP/UDP Services
  Enables enable/disable of services like Telnet, SSH, HTTP/S, SNMP
Storm Control
  Protects against network storms or floods in multi-switch environments
Denial of Service
  Predefined rules protect the network from malicious attacks
Notes: The simplest function is Port Security. This feature lets you lock down switch ports. Configures the port so that traffic from any other device physically connected to the port other than the "learned" one will be discarded. Forward is kind of the reverse of Discard in that if you move the "learned" device to any other port, it will be locked out. But data from any other device plugged into the "locked" port will be sent (or received) normally. The last option, Limited Learning, is handy if you have another small switch uplinked to the "locked" port. It will allow traffic to and from 16 MAC addresses, but then block traffic from anything else.
Another way to control LAN access is to have users actually log in or authenticate. Smart / managed switches usually support this option. Port Authentication controls, which include the ability to allow access if the RADIUS server is not available and the ability via the Guest VLAN setting to send anyone failing authentication to a particular VLAN. This technique effectively puts unknown users on a separate network from authenticated users and perhaps given only Internet access.
Storm Control is there to protect against network "storms" or floods of network traffic that are sometimes caused in large multiswitch networks. You have seen a network storm if you accidently connected two ports together on a switch and then saw the link / activity lights flash wildly.
Denial of Service Prevention s a set of predefined rules that protect the network from malicious attacks. Before activating Denial of Service Prevention, you typically must unbind all Access Control Lists (ACLs) or advanced QoS policies that are bound to a port. ACL and advanced QoS policies are not active when a port has Denial of Service Protection.

## Slide 16: Switch Management
Methods for management and monitoring include:
Command Line Interface (CLI)
Web-based management
SNMP (Simple Network Management Protocol)
  Standards-based management, easy to support
  Full managed switches typically support SNMP
RMON (Remote MONitoring)
  Enhances management capability
  Supports certain number of RMON ‘groups’
Notes: Most switches include some method for monitoring their performance so that you can proactively manage situations that may arise. The two most common methods are SNMP (Simple Network Management Protocol) and RMON (Remote MONitoring). SNMP has been around for a long time and is easy to support. Most fully managed switches have a management capability that supports SNMP.
Adding RMON capability to a switch greatly enhances management ability, however. When a switch has RMON capability, you’ll generally see that it supports a certain number of RMON “groups.” First, there are two versions of RMON, aptly named RMON1 and RMON2. Together they encompass 20 different groups of management statistics.
In general, when a switch supports RMON, at a minimum it will support the first four groups of RMON1: statistics, history, alarm, and event.

## Slide 17: Hot Swapping
Hot swapping is the ability to replace the various modules of a modular switch while the system is still operational and serving clients
Some hot-swap switches only let you swap modules of the same type
Notes: If you plan to regularly swap out modules and you want as little downtime as possible, you can opt for a switch that supports hot swapping. Hot swapping is the ability to replace the various modules of a modular switch while the system is still operational and serving clients. This is useful in 24/7 environments. Note that some hot-swap switches only let you swap modules of the same type. For example, you can’t hot-swap a 10/100 Ethernet module with a gigabit Ethernet module. You’d need to power down the unit for this swap.

## Slide 18: Switch PoE
802.3af vs. 802.3at PoE
  Only 802.3af PoE for Cisco Small Biz switches
  802.3at is planned for 5xx series
No Cisco inline power on Cisco Small Biz switches (only some „older“ Cisco products do support the Cisco inline power only – e.g. Some older phones)
Smart with PoE: ½ the ports at 7.5 Watt , ¼ of the ports at 15.4 Watt
SRW, SFE &SGE with PoE All ports at 7.5 Watt, ½ the ports at 15.4 Watts
Exception: SRW2xx8MP-K9 All ports at 15.4 Watt
Any possbible combination as long as the overall PoE budget is not exceeded

## Slide 19: Energy-Efficient Technology Auto Power-Down
Automatically turns off power on Gigabit Ethernet RJ-45 port when detecting link down
  If there is no link on a port (when there is no connection or the device connected is turned off), the port(s) enter a “sleep mode”
Resumes active mode when the switch detects the link up or device connected
  The switch sends out electrical pulses at frequent intervals
Adjusts power based on cable length (on Gigabit Ethernet models)
Detects the length of connected Ethernet cable and adjusts power usage accordingly—without affecting performance

## Slide 20: Switch Comparisons
Tolly Group: http://www.tolly.com/
Notes: Compare every product as fully as possible. Once you’ve chosen a switch, make sure the choice is a good one with a little specific follow-up research.
Tolly Group’s switching reports are an excellent resource to determine if the vendor’s specifications are realistic. Tolly tests almost every switch on the market and can say whether or not the numbers are accurate. Other groups also regularly test network equipment. My favorite resource to locate these kinds of reports is Google.