Jul  6 01:05:39.762: IPSEC:(SESSION ID = 1) (key_engine) request timer fired: count = 1,

(identity) local= 192.168.81.133:0, remote= 192.168.81.134:0,

local_proxy= 192.168.81.133/255.255.255.255/47/0,

remote_proxy= 192.168.81.134/255.255.255.255/47/0

Jul  6 01:05:39.763: IPSEC(sa_request): ,

(key eng. msg.) OUTBOUND local= 192.168.81.133:500, remote= 192.168.81.134:500,

local_proxy= 192.168.81.133/255.255.255.255/47/0,

remote_proxy= 192.168.81.134/255.255.255.255/47/0,

protocol= ESP, transform= esp-aes esp-sha256-hmac  (Tunnel),

lifedur= 3600s and 4608000kb,

spi= 0x0(0), conn_id= 0, keysize= 128, flags= 0x0

Jul  6 01:05:39.763: ISAKMP: (0):SA request profile is pf-isakmp-rsa2048-est

Jul  6 01:05:39.763: ISAKMP: (0):Created a peer struct for 192.168.81.134, peer port 500

Jul  6 01:05:39.763: ISAKMP: (0):New peer created peer = 0x80007FE3E644BC38 peer_handle = 0x80000000800001FA

Jul  6 01:05:39.763: ISAKMP: (0):Locking peer struct 0x80007FE3E644BC38, refcount 1 for isakmp_initiator

Jul  6 01:05:39.764: ISAKMP: (0):local port 500, remote port 500

Jul  6 01:05:39.764: ISAKMP: (0):set new node 0 to QM_IDLE

Jul  6 01:05:39.764: ISAKMP: (0):Find a dup sa in the avl tree during calling isadb_insert sa = 80007FE3E55707F8

Jul  6 01:05:39.764: ISAKMP: (0):Can not start Aggressive mode, trying Main mode.

Jul  6 01:05:39.764: ISAKMP-ERROR: (0):Profile has no keyring, aborting key search

Jul  6 01:05:39.764: ISAKMP-ERROR: (0):Profile has no keyring, aborting host key search

Jul  6 01:05:39.765: ISAKMP: (0):IKE->PKI Get configured TrustPoints state (I) MM_NO_STATE (peer 192.168.81.134)

Jul  6 01:05:39.765: ISAKMP: (0):PKI->IKE Got configured TrustPoints state (I) MM_NO_STATE (peer 192.168.81.134)

Jul  6 01:05:39.765: ISAKMP: (0):constructed NAT-T vendor-rfc3947 ID

Jul  6 01:05:39.766: ISAKMP: (0):constructed NAT-T vendor-07 ID

Jul  6 01:05:39.766: ISAKMP: (0):constructed NAT-T vendor-03 ID

Jul  6 01:05:39.766: ISAKMP: (0):constructed NAT-T vendor-02 ID

Jul  6 01:05:39.766: ISAKMP: (0):Input = IKE_MESG_FROM_IPSEC, IKE_SA_REQ_MM

Jul  6 01:05:39.766: ISAKMP: (0):Old State = IKE_READY  New State = IKE_I_MM1

Jul  6 01:05:39.766: ISAKMP: (0):beginning Main Mode exchange

Jul  6 01:05:39.766: ISAKMP-PAK: (0):sending packet to 192.168.81.134 my_port 500 peer_port 500 (I) MM_NO_STATE

Jul  6 01:05:39.766: ISAKMP: (0):Sending an IKE IPv4 Packet.

Jul  6 01:05:39.771: ISAKMP-PAK: (0):received packet from 192.168.81.134 dport 500 sport 500 Global (I) MM_NO_STATE

Jul  6 01:05:39.771: ISAKMP: (0):Input = IKE_MESG_FROM_PEER, IKE_MM_EXCH

Jul  6 01:05:39.771: ISAKMP: (0):Old State = IKE_I_MM1  New State = IKE_I_MM2

Jul  6 01:05:39.771: ISAKMP: (0):processing SA payload. message ID = 0

Jul  6 01:05:39.771: ISAKMP: (0):processing vendor id payload

Jul  6 01:05:39.771: ISAKMP: (0):vendor ID seems Unity/DPD but major 69 mismatch

Jul  6 01:05:39.771: ISAKMP: (0):vendor ID is NAT-T RFC 3947

Jul  6 01:05:39.771: ISAKMP: (0):Looking for xauth in profile pf-isakmp-rsa2048-est

Jul  6 01:05:39.772: ISAKMP: (0):IKE->PKI Get configured TrustPoints state (I) MM_NO_STATE (peer 192.168.81.134)

Jul  6 01:05:39.772: ISAKMP: (0):PKI->IKE Got configured TrustPoints state (I) MM_NO_STATE (peer 192.168.81.134)

Jul  6 01:05:39.772: ISAKMP: (0):Checking ISAKMP transform 1 against priority 10 policy

Jul  6 01:05:39.772: ISAKMP: (0):      encryption AES-CBC

Jul  6 01:05:39.772: ISAKMP: (0):      keylength of 128

Jul  6 01:05:39.772: ISAKMP: (0):      hash SHA256

Jul  6 01:05:39.772: ISAKMP: (0):      default group 14

Jul  6 01:05:39.772: ISAKMP: (0):      auth RSA sig

Jul  6 01:05:39.772: ISAKMP: (0):      life type in seconds

Jul  6 01:05:39.772: ISAKMP:      life duration (VPI) of  0x0 0x1 0x51 0x80

Jul  6 01:05:39.772: ISAKMP: (0):atts are acceptable. Next payload is 0

Jul  6 01:05:39.772: ISAKMP: (0):Acceptable atts:actual life: 0

Jul  6 01:05:39.772: ISAKMP: (0):Acceptable atts:life: 0

Jul  6 01:05:39.772: ISAKMP: (0):Fill atts in sa vpi_length:4

Jul  6 01:05:39.772: ISAKMP: (0):Fill atts in sa life_in_seconds:86400

Jul  6 01:05:39.772: ISAKMP: (0):IKE->PKI Start PKI Session state (I) MM_NO_STATE (peer 192.168.81.134)

Jul  6 01:05:39.772: CRYPTO_PKI: (9023B) Session started - identity not specified

Jul  6 01:05:39.772: ISAKMP: (0):PKI->IKE Started PKI Session state (I) MM_NO_STATE (peer 192.168.81.134)

Jul  6 01:05:39.772: ISAKMP: (0):Returning Actual lifetime: 86400

Jul  6 01:05:39.772: ISAKMP: (0):Started lifetime timer: 86400.

Jul  6 01:05:39.772: ISAKMP: (0):processing vendor id payload

Jul  6 01:05:39.772: ISAKMP: (0):vendor ID seems Unity/DPD but major 69 mismatch

Jul  6 01:05:39.773: ISAKMP: (0):vendor ID is NAT-T RFC 3947

Jul  6 01:05:39.773: ISAKMP: (0):Input = IKE_MESG_INTERNAL, IKE_PROCESS_MAIN_MODE

Jul  6 01:05:39.773: ISAKMP: (0):Old State = IKE_I_MM2  New State = IKE_I_MM2

Jul  6 01:05:39.773: ISAKMP: (0):IKE->PKI Get configured TrustPoints state (I) MM_SA_SETUP (peer 192.168.81.134)

Jul  6 01:05:39.773: ISAKMP: (0):PKI->IKE Got configured TrustPoints state (I) MM_SA_SETUP (peer 192.168.81.134)

Jul  6 01:05:39.773: ISAKMP: (0):IKE->PKI Get IssuerNames state (I) MM_SA_SETUP (peer 192.168.81.134)

Jul  6 01:05:39.773: ISAKMP: (0):PKI->IKE Got IssuerNames state (I) MM_SA_SETUP (peer 192.168.81.134)

Jul  6 01:05:39.773: ISAKMP: (0):constructing CERT_REQ for issuer cn=TEST INTERMEDIATE CA 53,ou=Stuff,ou=myOU,o=myOrg,c=US

Jul  6 01:05:39.773: ISAKMP: (0):constructing CERT_REQ for issuer cn=Test Root CA 3,ou=Stuff,ou=myOU,o=myOrg,c=US

Jul  6 01:05:39.773: ISAKMP-PAK: (0):sending packet to 192.168.81.134 my_port 500 peer_port 500 (I) MM_SA_SETUP

Jul  6 01:05:39.773: ISAKMP: (0):Sending an IKE IPv4 Packet.

Jul  6 01:05:39.774: ISAKMP: (0):Input = IKE_MESG_INTERNAL, IKE_PROCESS_COMPLETE

Jul  6 01:05:39.774: ISAKMP: (0):Old State = IKE_I_MM2  New State = IKE_I_MM3

Jul  6 01:05:39.804: ISAKMP-PAK: (0):received packet from 192.168.81.134 dport 500 sport 500 Global (I) MM_SA_SETUP

Jul  6 01:05:39.804: ISAKMP: (0):Input = IKE_MESG_FROM_PEER, IKE_MM_EXCH

Jul  6 01:05:39.804: ISAKMP: (0):Old State = IKE_I_MM3  New State = IKE_I_MM4

Jul  6 01:05:39.805: ISAKMP: (0):processing KE payload. message ID = 0

Jul  6 01:05:39.807: ISAKMP: (0):processing NONCE payload. message ID = 0

Jul  6 01:05:39.807: ISAKMP: (1477):processing vendor id payload

Jul  6 01:05:39.807: ISAKMP: (1477):vendor ID is Unity

Jul  6 01:05:39.807: ISAKMP: (1477):processing vendor id payload

Jul  6 01:05:39.807: ISAKMP: (1477):vendor ID is DPD

Jul  6 01:05:39.807: ISAKMP: (1477):processing vendor id payload

Jul  6 01:05:39.807: ISAKMP: (1477):speaking to another IOS box!

Jul  6 01:05:39.807: ISAKMP: (1477):received payload type 20

Jul  6 01:05:39.807: ISAKMP: (1477):His hash no match - this node outside NAT

Jul  6 01:05:39.807: ISAKMP: (1477):received payload type 20

Jul  6 01:05:39.807: ISAKMP: (1477):No NAT Found for self or peer

Jul  6 01:05:39.807: ISAKMP: (1477):Input = IKE_MESG_INTERNAL, IKE_PROCESS_MAIN_MODE

Jul  6 01:05:39.807: ISAKMP: (1477):Old State = IKE_I_MM4  New State = IKE_I_MM4

Jul  6 01:05:39.807: ISAKMP: (1477):processing CERT_REQ payload.

Jul  6 01:05:39.808: ISAKMP: (1477):peer wants a CT_X509_SIGNATURE cert

Jul  6 01:05:39.808: ISAKMP: (1477):peer wants cert issued by cn=TEST INTERMEDIATE CA 53,ou=Stuff,ou=myOU,o=myOrg,c=US

Jul  6 01:05:39.808: CRYPTO_PKI: Trust-Point tp-rsa2048-est picked up

Jul  6 01:05:39.808: CRYPTO_PKI: 1 matching trustpoints found

Jul  6 01:05:39.808: ISAKMP: (1477):processing CERT_REQ payload.

Jul  6 01:05:39.808: ISAKMP: (1477):peer wants a CT_X509_SIGNATURE cert

Jul  6 01:05:39.808: ISAKMP: (1477):peer wants cert issued by cn=Test Root CA 3,ou=Stuff,ou=myOU,o=myOrg,c=US

Jul  6 01:05:39.808: CRYPTO_PKI: Trust-Point tp-rsa2048-est picked up

Jul  6 01:05:39.808: CRYPTO_PKI: 1 matching trustpoints found

Jul  6 01:05:39.808: CRYPTO_PKI: (8023C) Session started - identity selected (tp-rsa2048-est)

Jul  6 01:05:39.808: ISAKMP: (1477):Choosing trustpoint tp-rsa2048-est as issuer

Jul  6 01:05:39.808: CRYPTO_PKI: Rcvd request to end PKI session 8023C.

Jul  6 01:05:39.808: CRYPTO_PKI: PKI session 8023C has ended. Freeing all resources.

Jul  6 01:05:39.808: CRYPTO_PKI: unlocked trustpoint tp-rsa2048-est, refcount is 0

Jul  6 01:05:39.808: CRYPTO_PKI: locked trustpoint tp-rsa2048-est, refcount is 1

Jul  6 01:05:39.808: CRYPTO_PKI: Identity bound (tp-rsa2048-est) for session 9023B

Jul  6 01:05:39.808: ISAKMP: (1477):IKE->PKI Get self CertificateChain state (I) MM_KEY_EXCH (peer 192.168.81.134)

Jul  6 01:05:39.808: ISAKMP: (1477):PKI->IKE Got self CertificateChain state (I) MM_KEY_EXCH (peer 192.168.81.134)

Jul  6 01:05:39.809: ISAKMP-ERROR: (1477):Unable to get router cert or routerdoes not have a cert: needed to find DN!

Jul  6 01:05:39.809: ISAKMP: (1477):SA is doing

Jul  6 01:05:39.809: ISAKMP: (1477):RSA signature authentication using id type ID_IPV4_ADDR

Jul  6 01:05:39.809: ISAKMP: (1477):ID payload

next-payload : 6

type         : 1

Jul  6 01:05:39.809: ISAKMP: (1477):    address      : 192.168.81.133

Jul  6 01:05:39.809: ISAKMP: (1477):    protocol     : 17

port         : 500

length       : 12

Jul  6 01:05:39.809: ISAKMP: (1477):Total payload length: 12

Jul  6 01:05:39.809: ISAKMP: (1477):IKE->PKI Get CertificateChain to be sent to peer state (I) MM_KEY_EXCH (peer 192.168.81.134)

Jul  6 01:05:39.809: ISAKMP: (1477):PKI->IKE Got CertificateChain to be sent to peer state (I) MM_KEY_EXCH (peer 192.168.81.134)

Jul  6 01:05:39.809: ISAKMP-ERROR: (1477):unable to build cert chain

Jul  6 01:05:39.810: ISAKMP-ERROR: (1477):(1477): FSM action returned error: 2

Jul  6 01:05:39.810: ISAKMP: (1477):Input = IKE_MESG_INTERNAL, IKE_PROCESS_COMPLETE