## Slide 1: Restrict guest endpoint to 1hr per 24hr period Use Case example: airports/hotels
Access based on guest type:
Self-reg granted 1 hour
sponsor created accounts ex: 8 hrs
Use Hotspot portal to give a restricted message
Purging set to 1 day (24 hrs) or days
Flow
Users logs into portal, device is registered
Device gets internet access (guestendpoint with a portaluser)
Account expires, COA sends endpoint to blocked message portal
When device is purged then can login again with same device

## Slide 2: Restrict guest endpoint to 1hr per 24hr period Guest Access > Configure > GuestTypes > Add Guest Type
Guest Type Changes
change maximum account duration
Max devices no change
ChangeEndpoint group if using special group
Purge endpoint set to 1 day

## Slide 3: Restrict guest endpoint to 1hr per 24hr period Admin > Identity Mgmt > Groups > Endpoint ID Groups > Add Special Endpoint Group

## Slide 4: Restrict guest endpoint to 1hr per 24hr period Authorization Profile for Guest Permit > Session Timeout
Radius-Session-Timeout
Permit Access Authorization use 900s(15m) to block close to 1hr
Create another profile for BlockMessage use 3600s(1h)

## Slide 5: Restrict guest endpoint to 1hr per 24hr period Authorization Policy
After account expires/suspended/deleted the device is removed from Endpoint Group
Since its still a known endpoint we are able to redirect to a message portal
but still profiled as its known endpoint

## Slide 6: Restrict guest endpoint to 1hr per 24hr period Valid User info

## Slide 7: Restrict guest endpoint to 1hr per 24hr period Suspended/Expired – to re-register need to clear the endpoint

## Slide 8: Restrict guest endpoint to 1hr per 24hr period RADIUS Livelog

## Slide 9: Restrict access 8hrs out of 23 using AUP
Use Hotspot portal to give a restricted message
supports entry of AUP hour value greater than 7 or less than 23
Set by endpointgroup (not guest-type)
Flow:
User accesses network, redirected to hotspot accepts AUP
After 8 hrs > Device Re-auth happens per session time-out (or device has left and comes back)
Device gets new authorization redirect to blocked message
After 23 hrs is able to register endpoint again
For Your Reference

## Slide 10: Restrict access 8hrs out of 23 using AUP Authorization Policy
For Your Reference

## Slide 11: Restrict access 8hrs out of 23 using AUP Authorization Profile for Guest Permit > Session Timeout
AuthzProfilePermitAccess:
RADIUS-Request for re-auth for 900s(15m) to block close to 1 hr mark
set higher if not critical to disconnect close to mark
AuthzProfileBlockRedirect:
Use 3600s(1 h) for BlockMessagePortal
For Your Reference

## Slide 12: Restrict access 8hrs out of 23 using AUP RADIUS Livelog
Endpoint Details
AUP Value stops at 23
For Your Reference